## Slide 1: Achieving energetic particle confinement in stellarators with precise quasisymmetry
M Landremana, A Cerfonb, M Drevlakc, A Giulianib, B Medasanid, E J Pauld, G Stadlerb, F Wechsungb, C Zhue
a U of Maryland, b New York U, c Max Planck Institute for Plasma Physics, d PPPL, e U of Science & Technology of China
Landreman & Paul, PRL (2022), Wechsung et al, PNAS (2022)
Notes: ~/Box Sync/work22/20220304-01-animated_gifs_for_simons_talk/20220304-01-001_simsopt_QH_beta0p05_animated_gif
~/Box Sync/work22/20220304-01-animated_gifs_for_simons_talk/20220304-01-002-preciseQAWithWellFromSimsopt_animated_gif

## Slide 2
Advantages of stellarators: steady-state, no disruptions, no Greenwald density limit, no power recirculated for current drive.
But, alpha particle losses & collisional transport would be too large unless you carefully choose the geometry.
Magnetic field lines
Notes: m20191005_01_plotHSXForEFTCTalk.m
m20191111_01_QHSIllustrationWithMagneticAxis_edited.png
m20210315_01_QHSIllustrationWithMagneticAxis_a

## Slide 3
Remarkable progress in stellarator confinement in the last year
All configurations scaled to same minor radius and |B|.
See also Bader et al, Nuclear Fusion (2021).
Notes: 20220323-01-alphaLossBarChart_nr600_nphi400_nz401

## Slide 4
Advantages of stellarators: steady-state, no disruptions, no Greenwald density limit, no power recirculated for current drive.
But, alpha particle losses & collisional transport would be too large unless you carefully choose the geometry.
A solution: quasisymmetry
Boozer angles
B = B(s, 𝜃 − N 𝜑)
𝜃
𝜑
Constant s = normalized toroidal flux
Magnetic field lines
Notes: m20191005_01_plotHSXForEFTCTalk.m
m20191111_01_QHSIllustrationWithMagneticAxis_edited.png
m20210315_01_QHSIllustrationWithMagneticAxis_a

## Slide 5
Since 2021
ML & Paul,
Phys Rev Lett (2022)
Wechsung et al,
PNAS (2022)
Giuliani et al,
1-stage, arXiv (2022)
Nies & Paul
Adjoint method
5% 𝛽, Self-consistent plasma current
Near-axis expansion
Quasi-axisymmetry (QA)
N = 0
Quasi-helical symmetry (QH)
N ≠ 0
Goal: B = B(s, 𝜃 − N 𝜑)
Notes: ~/Box Sync/work21/20210711-01-imperfect_symmetry_figure/20210711-01-007-imperfect_symmetry_figure_8x1
Colorbar: Box Sync/work22/20220126-01-BOnSurfacesForWechsungPreciseQACoilsPaper/20220126-01-004_BOnSurfacesForWechsungPreciseQACoilsPaper
~/Box Sync/work22/20220304-02-recent_QS_configs_for_Simons_talk

## Slide 6
Optimizing stellarator geometry for precise quasisymmetry
Self-consistent bootstrap current
Conclusions

## Slide 7
Optimizing stellarator geometry for precise quasisymmetry
Self-consistent bootstrap current
Conclusions

## Slide 8: Optimization problem
2 stage approach, as for W7-X: First optimize shape of boundary surface, then coils.
Objective functions:
Boundary aspect ratio
For quasi-axisymmetry,
N = 0.
For quasi-helical symmetry,
N is the “number of field periods”,
e.g. N = 4
here
Goal: B = B(s, 𝜃 − N 𝜑).

## Slide 9: Optimization problem
2 stage approach, as for W7-X: First optimize shape of boundary surface, then coils.
Objective functions:
Parameter space: Rm,n & Zm,n defining a toroidal boundary
Codes used: SIMSOPT with VMEC
Cold start: circular cross-section torus
Vacuum fields at first, allowing precise checks
Algorithm: default for least-squares in scipy (trust region reflective)
6 steps: increasing # of modes varied & VMEC resolution
Run many optimizations, pick the best
Boundary aspect ratio

## Slide 10: Straight |B| contours are possible for quasi-axisymmetry
aspect = 6
ML & Paul, PRL (2022).

## Slide 11: Straight |B| contours are possible for quasi-helical symmetry
aspect = 8
ML & Paul, PRL (2022).

## Slide 12: Good symmetry also exists with magnetic well
aspect = 6
QA
QH
ML & Paul, PRL (2022).
Notes: 20210730-01-precise_QA_magwell_surfaces.pdf
m20210730_01_plotPreciseQAWithWell_3D.m

## Slide 13: 16-coil solutions have been found for the quasi-axisymmetric configurations
Wechsung et al, PNAS (2022). <R> / 10 between filament centers. Haven’t looked at the QHs yet
With magnetic well
Without magnetic well
Notes: ~/Box Sync/work21/20211103-01-simsopt_coils_from_Florian/20211103-01-precise_QA_coil_animation

## Slide 14: Symmetry-breaking modes can be made extremely small
New QA configuration
Dotted = with coils
Notes: ~/Box Sync/work21/20211105-01-compareSymmetryBreakingVsRadius_withCoils
# 20210904-04-compareSymmetryBreakingVsRadius_withQHMagwell_noGeomag
20211105-01-compareSymmetryBreakingVsRadius_withCoils
Cobra:
/ptmp/mlan/20210721-01-eps_eff_for_precise_QS_configs/20210721-01-compareEpsEffAcrossConfigs.pdf

## Slide 15: Quasisymmetry works: alpha particle confinement is significantly improved
All configs scaled to minor radius and |B| of ARIES-CS
Fusion alpha birth distribution
ANTS code, with collisions
Particle considered lost when s > 1
Notes: 20220323-01-alphaLossBarChart_nr600_nphi400_nz401

## Slide 16: Alpha confinement in quasi-helical stellarators can be better than in a tokamak due to thinner bananas
See poster by Elizabeth Paul (session 3)
QA+well
QA
QH+well
QH
Notes: 20220323-01-alphaLossBarChart_nr600_nphi400_nz401

## Slide 17
Optimizing stellarator geometry for precise quasisymmetry
Self-consistent bootstrap current
Conclusions

## Slide 18: How can bootstrap current be included self-consistently in stellarator optimization?
Need self-consistency between MHD equilibrium and drift-kinetic equation.
Previous method: fixed-point iteration, only after an optimization.
Accurate drift-kinetic bootstrap calculations in stellarators are computationally expensive. Preferably not in the optimization loop.
VMEC: given I0(s), determine B0.
SFINCS: given B0, determine I1(s).
VMEC: given I1(s), determine B1.
SFINCS: given B1, determine I2(s).
…
Normalized toroidal flux s
MHD equilibrium code
Drift-kinetic code

## Slide 19: New idea: exploit quasisymmetry & use analytic expressions for tokamaks
Pytte & Boozer (1981), Boozer (1983):
Bootstrap current (& other quantities) in quasisymmetry are the same as in axisymmetry, up to some substitutions:
Should be accurate for the new precisely quasisymmetric configurations.

## Slide 20: New idea: exploit quasisymmetry & use analytic expressions for tokamaks
Pytte & Boozer (1981), Boozer (1983):
Bootstrap current (& other quantities) in quasisymmetry are the same as in axisymmetry, up to some substitutions:
Should be accurate for the new precisely quasisymmetric configurations.

## Slide 21: Before doing new optimizations: Redl formula is accurate in previous QA & QH stellarators
<J dot B> [MA T / m2]
<J dot B> [MA T / m2]
QA (Landreman & Paul (2021))
Normalized toroidal flux s
Normalized toroidal flux s
QH (Landreman & Paul (2021))
(Not self-consistent yet)
Redl analytic formula
SFINCS kinetic code
ne = (1 – s5) 4x1020 m-3, Te = Ti = (1 – s) 12 keV
Notes: 20211225-01 Lab book - sfincs Redl benchmarks.docx

## Slide 22: Optimization recipe
Objective function:
Parameter space: {Rm,n, Zm,n, toroidal flux, current spline values}
or {Rm,n, Zm,n, toroidal flux, iota spline values}
Cold start
Algorithm: default for least-squares in scipy (trust region reflective)
Steps: increasing # of modes varied: m and |n/nfp| up to j in step j
Boundary aspect ratio
Minor radius

## Slide 23: Example of optimization with self-consistent bootstrap current
ne0 = 2.5e20/meters3
Te0 = Ti0 = 10 keV
𝛽 = 2.8%,
Ip = 1.3 MA
Notes: wout_20220102-01-012_QH_A6.5_n0_2.5_T0_10_abs_step_1.00e-08_rel_step_3.16e-05_centered.nc
20220110-01-compareMethodsOfComputingJDotBForOptimizedSelfConsistentQH

## Slide 24: If you want perfectly self-consistent current, you can do a few fixed-point iterations at the end
No significant degradation in quasisymmetry:
Optimization with Redl current
After SFINCS fixed-point iterations
𝛼 energy losses < 0.3%
VMEC
SFINCS (kinetic bootstrap calculation)
Notes: 20220117-02-vmecSfincsConsistencyForQHBeta5
boozPlot4Surfs
boozmn_20220102-01-050_QH_nfp4_A6p5_n0_3_T0_15_beta0p05_hires_4surfs.pdf
boozmn_20220102-01-053_iteratingVmecAndSfincsForBestFrom048_003_4surfs.pdf

## Slide 25
Optimizing stellarator geometry for precise quasisymmetry
Self-consistent bootstrap current
Conclusions

## Slide 26
It is now possible to design stellarators with alpha confinement comparable to or better than a tokamak.
𝛼 energy loss fraction:
More to do: coils, surface quality, & MHD stability at high 𝛽, robustness to pressure profile, ...
Notes: ~/Box Sync/work22/20220304-01-animated_gifs_for_simons_talk/20220304-01-001_simsopt_QH_beta0p05_animated_gif
~/Box Sync/work22/20220304-01-animated_gifs_for_simons_talk/20220304-01-002-preciseQAWithWellFromSimsopt_animated_gif

## Slide 27: Extra slides

## Slide 28: The bootstrap current arises in tokamaks & stellarators when the density & temperature become significant
Ions and electrons have different trajectories. Different mean flows = electric current.
Current depends on geometry, density, & temperature.
For 𝛽 > 0, we don’t know B until we include this effect.
Computing the bootstrap current requires kinetic theory: coupled 4D advection-dominated integro-differential equations.
Need self-consistency between MHD equilibrium and kinetic equation.
How can a self-consistent bootstrap current calculation be integrated with stellarator optimization?
electron
ion

## Slide 29: The symmetry also yields extremely low collisional transport for a thermal plasma
Dotted = with coils
Radial neoclassical transport coefficient
Wechsung et al, PNAS (2022)
Notes: # 20210721-01-compareEpsEffAcrossConfigs_magwell.pdf
/ptmp/mlan/20211030-01-coils_for_precise_quasisymmetry/20211030-01-compareEpsEffAcrossConfigs_withCoils2

## Slide 30: The optimization with self-consistent bootstrap current also works for quasi-axisymmetry
Symmetry is not as good as for vacuum, but sufficient for excellent confinement
Possible islands where 𝜄 = 2/3,
𝜄 = 4/7 = 0.57?
VMEC
SFINCS (kinetic bootstrap calculation)
𝛼-particle losses < 1%
Notes: m20210604_01_plotVMECWout_withFieldlineSeamAtBottom.m with wout_20220218-01-014-005_QA_nfp2_beta0p03_iotaTarget0p7.nc
~/Box Sync/work22/boozmn_20220218-01-014-005_QA_nfp2_beta0p03_iotaTarget0p7_4surfs.pdf
20220302-01-vmecSfincsConsistencyForQA_beta3_iotaTarget0p7
20220302-02-plotIotaProfileForFiniteBetaSimsoptQA

## Slide 31: |B|in Boozer coordinates was verified by independent SPEC calculations
By Elizabeth Paul
Boozer toroidal angle
Boozer poloidal angle
max |Bm,n| [Tesla] with n ≠ 0
(Ntor = Mpol, Lrad = Mpol + 4)

## Slide 32: To reach reactor-relevant 5% beta in QH without crossing iota=1, a constraint on iota can be included
Crossing iota=1, the worst resonance, is probably unacceptable.
𝛽 = 0
𝛽 = 5%
ne0 = 3e20/meters3, Te0 = Ti0 = 15 keV
Notes: 20220117-03-plotIotaProfilesForFiniteBetaSimsoptQHs_withoutBest

## Slide 33: To reach reactor-relevant 5% beta in QH without crossing iota=1, a constraint on iota can be included
Crossing iota=1, the worst resonance, is probably unacceptable.
𝛽 = 0
𝛽 = 5%
𝛽 = 5% with 𝜄 barrier
Solution: Add barrier term in objective
Quasisymmetry & bootstrap consistency remain good:
Normalized toroidal flux s
Notes: 20220117-01-plotIotaProfilesForFiniteBetaSimsoptQHs
boozPlot4Surfs
boozmn_20220102-01-050_QH_nfp4_A6p5_n0_3_T0_15_beta0p05_hires_4surfs.pdf
20220116-01-compareMethodsOfComputingJDotBForOptimizedSelfConsistentQH_beta5 with config=1
20220302-02-plotIotaProfileForFiniteBetaSimsoptQA

## Slide 34: Why do the configurations with best quasisymmetry not have the best trajectory confinement?
QA + magnetic well
QA
Lost trajectories in the new QA look like this:
Fraction of
alpha energy lost
QH
Notes: # 20210721-02-compareSimpleResultsAcrossConfigs_topFew.pdf
20210719-01-117_beams3d_new_QA_aScaling_losses.pdf
20220106-01-plot_ANTS_config_comparison_topFew.pdf

## Slide 35: 2 types of quasisymmetry
Contours of B = |B|:
Notes: ~/Box Sync/work21/20211115-01-illustration_of_QA_QH_for_talk

## Slide 36: Previous quasisymmetric configurations
Is there an optimization recipe that can give consistently straight |B| contours?
(a) Zarnstorff et al (2001)
(b) Najambadi et al (2008)
(c) Garabedian (2008)
(d) Liu et al (2018)
(e) Henneberg et al (2019)
(f) Nuhrenberg & Zille (1988)
(g) Anderson et al (1995)
(h) Bader et al (2020)
We want
B = B(r, 𝜃 − N 𝜑)

## Slide 37: The new configurations have small magnetic shear
New QH
New QA
VMEC
...... SPEC

## Slide 38: New idea: exploit quasisymmetry & use analytic expressions for tokamaks
Redl (2021)
NEO = kinetic calculation
Geometry enters through
Flux surface label (minor radius)
Bootstrap current

## Slide 39: The symmetry yields extremely good confinement of collisionless trajectories
All configurations scaled to ARIES-CS minor radius (1.7 m) and |B| (5.7 T).
5000 alpha particles initialized isotropically at s=0.3.
SIMPLE code: Albert et al, JCP (2020).
New QA with coils
New QA+well with coils
Wistell-A
New QH, New QH+well
Notes: /ptmp/mlan/20211030-01-coils_for_precise_quasisymmetry/20211030-01-compareSimpleResultsAcrossConfigs_withCoils2
# 20210721-02-compareSimpleResultsAcrossConfigs_magwell.pdf

## Slide 41: Previous quasisymmetric configurations (s=0.5)
Notes: ~/Box Sync/work21/20210711-01-imperfect_symmetry_figure/20210711-01-005_B_along_fieldlines_previous_configs_s0.5.pdf

## Slide 42: Previous quasisymmetric configurations (s=1)
Notes: ~/Box Sync/work21/20210711-01-imperfect_symmetry_figure/20210711-01-005_B_along_fieldlines_previous_configs_s1.pdf

## Slide 43: |B| along a field line for new QA
Notes: ~/Box Sync/work21/20210720-03-plot_B_along_field_line_for_precise_QA

## Slide 44: |B| along a field line for new QH
Notes: ~/Box Sync/work21/20210720-04-plot_B_along_field_line_for_precise_QH

## Slide 45: |B| along a field line for new QA with magnetic well
Notes: ~/Box Sync/work21/20210801-01-plot_B_along_field_line_for_precise_QA_magwell

## Slide 46: SPEC confirms the new QA/QH configurations have good surfaces
New QH
New QA
New
QA+well
VMEC
...... SPEC
New QH+well
Notes: 20210704-01-065_new_QA_plot_spec_and_vmec.png
20210704-01-064_new_QH_plot_spec_and_vmec.png
20210728-01-013_new_QA_magwell_plot_spec_and_vmec.png
20210728-01-029_new_QH_magwell_plot_spec_and_vmec.png

## Slide 47: Good flux surface exist with coils
New QA
New QA+well

## Slide 48: Future directions
Eliminate islands at high 𝛽 (plasma pressure & current)
Coils & MHD stability for the high 𝛽 configurations
Quasi-isodynamic (|B| contours close poloidally)
Understand trade-offs using multi-objective optimization
Robustness to uncertainty in the pressure profile
Interact with systems codes & reactor studies
Combined coil + confinement (1-stage) optimization
Optimization of turbulence & divertor
...... SPEC
Before optimization
After optimization
ML, Medasani & Zhu (2021)