## Slide 1: Some numerical topics in stellarator optimization
Matt Landreman, UMD, Institute for Research in Electronics & Applied Physics (IREAP)
David Bindel1, Stefan Buller2, Bill Dorland2, Rogerio Jorge3, Alan Kaptanoglu2, Patrick Kim2, Noah Mandell4, Misha Padidar1, Elizabeth Paul5
1 Cornell, 2 UMD, 3 IST Lisbon, 4 Princeton Plasma Physics Laboratory, 5 Columbia

## Slide 2: Magnetic fields can be used to confine charged particles & plasma
Magnetic field line
Charged particle (electron or ion)
There is no confinement along the magnetic field, so bend it into a torus.

## Slide 3: A stellarator is a configuration of magnets for confining plasma without continuous rotation symmetry
Electromagnetic coils
Magnetic surfaces, plasma
Magnetic field lines
Particle trajectory
Axisymmetry (tokamak) requires large current in plasma: hard to sustain, unstable, sometimes impossible.

## Slide 4: A stellarator is a configuration of magnets for confining plasma without continuous rotation symmetry
Electromagnetic coils
Magnetic surfaces, plasma
Magnetic field lines
Particle trajectory
Applications:
Fusion energy
Particle trap for basic physics

## Slide 5: Example: W7-X (Germany)
Clery, Science (2022)

## Slide 7: Stellarator plasma & coil shapes can be optimized for several objectives
Field lines lie on nested 2D toroidal surfaces, not volume-filling
Good confinement of particle trajectories
Buildable coil shapes
Any plasma current doesn’t modify B too much
Magnetohydrodynamic stability
Reduced turbulence
Electromagnetic coils
Magnetic surfaces, plasma
Magnetic field lines

## Slide 8: Outline
Optimizing plasma shape, directly targeting particle confinement.
Optimizing plasma shape using a surrogate (“quasisymmetry”)
Optimizing plasma shape to reduce turbulence
Topology optimization for magnets

## Slide 9: Outline
Optimizing plasma shape, directly targeting particle confinement.
Optimizing plasma shape using a surrogate (“quasisymmetry”)
Optimizing plasma shape to reduce turbulence
Topology optimization for magnets

## Slide 10: For plasma shape optimization, parameter space is usually Fourier amplitudes of the boundary surface
Room for innovation here…
Shape of boundary surface determines the magnetic field B inside (up to scale factor).
Without plasma: in , on .
With plasma: Also need to specify pressure & current on each interior surface.
Notes: m20191005_01_plotHSXForEFTCTalk.m

## Slide 11: Charged particle trajectories can be simulated accurately using “guiding center” ODEs
Magnetic field line
Particle trajectory
Guiding center trajectory
Su et al (2020)

## Slide 12: Charged particle trajectories can be simulated accurately using “guiding center” ODEs
Su et al (2020)
Fraction of particles lost in various stellarators

## Slide 13: Direct optimization of particle confinement is challenging due to computational cost & noise
Energy loss, integrating over initial conditions (objective function)
MC, 32,000 particles
4096 particles
Bindel, ML, Padidar, arXiv (2023)
Line through parameter space

## Slide 14: Improvement in confinement can be achieved with this direct approach
Bindel, ML, Padidar, arXiv (2023)
Fraction of particles lost
Energy losses
Other stellarator shapes
Notes: See https://github.com/mishapadidar/alpha_particle_opt/blob/main/experiments/plot/make_loss_profile_data.py
The A and B configurations are (respectively)
nfp4_QH_cold_high_res_phase_one_mirror_1.35_aspect_7.0_iota_0.89
nfp4_QH_cold_high_res_phase_one_mirror_1.35_aspect_7.0_iota_1.043

## Slide 15: Outline
Optimizing plasma shape, directly targeting particle confinement.
Optimizing plasma shape using a surrogate (“quasisymmetry”)
Optimizing plasma shape to reduce turbulence
Topology optimization for magnets

## Slide 16: Quasisymmetry is a sufficient (though not necessary) condition for confinement, & a useful surrogate
“Boozer angles”
B = B(s, 𝜃 − N 𝜑)
𝜃
𝜑
Constant s = normalized toroidal flux
Magnetic field lines
Boundary aspect ratio
For quasi-axisymmetry,
N = 0.
For quasi-helical symmetry,
N is the number of field periods,
e.g.
N = 4
here
Objective:

## Slide 17: Example of quasi-axisymmetry optimization
ML & Paul, Phys Rev Lett (2022)
Optimization details:
Default algorithm in scipy for nonlinear least-squares (“trust region reflective”)
Initialize with circular cross-section torus.
Gradients from finite differences or automatic differentiation.
Expand the number of Fourier modes in the parameter space in steps. 8-120 design variables.

## Slide 18: Example of quasi-helical symmetry optimization
ML & Paul, Phys Rev Lett (2022)

## Slide 19: Quasisymmetry has been an effective surrogate for finding plasma shapes with good confinement, though it might be too limiting.
Since 2021
Trajectories of fusion-produced distribution of alpha particles followed in many magnetic configurations, all scaled to reactor size and |B|:
Fraction of alpha-particle energy lost before thermalization
Multi-fidelity method with quasisymmetry + direct ODE integration?

## Slide 20: Outline
Optimizing plasma shape, directly targeting particle confinement.
Optimizing plasma shape using a surrogate (“quasisymmetry”)
Optimizing plasma shape to reduce turbulence
Topology optimization for magnets

## Slide 21: Shape optimization to reduce plasma turbulence would be valuable but is hard
Gradients of plasma density & temperature cause instabilities & turbulence.
Causes heat to leak out.
Known to depend on plasma shape.
Turbulence simulations: ~10 GPU-min to 106s of CPU-hours.
5D + time
No agreed-upon surrogate like Reynolds-averaged Navier-Stokes + closure yet.
Nunami 2012
Notes: Turbulence image from http://fusionsites.ciemat.es/gyrokineticsmadrid2014/files/2014/06/Nunami.pdf
From https://aip.scitation.org/doi/pdf/10.1063/1.4704568 Nunami et al., PoP 19, 042504 (2012)

## Slide 22: One approach to optimizing turbulence: minimize linear growth rate of instabilities
Jorge et al, arXiv (2023)
Linear growth rate gives a smooth, deterministic, non-chaotic objective
time
Heat flux out of the plasma
Stellarator optimized for only quasisymmetry
Linear phase
Stellarator also optimized for linear growth rate
Stellarator optimized for only quasisymmetry
Stellarator also optimized for linear growth rate
But linear growth rate is not a perfect predictor of the nonlinear heat flux…

## Slide 23: First optimizations with nonlinear turbulence calculations in the objective
By Patrick Kim (UMD undergraduate!)
Bayesian optimization with 20-100 design variables would be nice…
Using stochastic gradient descent with momentum
time

## Slide 24: Outline
Optimizing plasma shape, directly targeting particle confinement.
Optimizing plasma shape using a surrogate (“quasisymmetry”)
Optimizing plasma shape to reduce turbulence
Topology optimization for magnets

## Slide 25: An established method for electromagnetic coil design is available, but has some limitations
Assume plasma shape has already been optimized, so target B field is known.
Coils represented as space curves.
Design variables: Fourier modes of Cartesian components.
Objective:
Issues:
Non-convex, so there are multiple local minima. Need good initial guess.
Coil topology & number of coils are fixed by initial guess.
+…
Match target B
Regularization

## Slide 26: New topology optimization method for electromagnetic coils
Pre-define grid of voxels where current might flow.
Current density J in each voxel represented by basis of 11 divergence-free functions. Amplitudes are the design variables.
Current conservation at each cell face gives linear equality constraints.
Given basis functions, B can be computed by Biot-Savart Law:
Without sparsity-promoting terms, problem is linear.
With l1 sparsity, problem remains convex.
With l0 sparsity, good algorithms exist.
Match target B
Regularization
Objective:
Work by Alan Kaptanoglu

## Slide 27: Preliminary results from electromagnet topology optimization: In axisymmetry, expected currents are recovered

## Slide 28: Preliminary results from electromagnet topology optimization: With sparsity objective, currents coalesce into discrete coils

## Slide 29: Preliminary results from electromagnet topology optimization: Starting to look at non-axisymmetric geometries

## Slide 30: Conclusions: stellarator optimization is a subject with many challenging numerical problems
This talk:
Shape optimization for confining particle trajectories, with PDE & possibly ODE solves.
Shape optimization with linear stability or nonlinear turbulence simulations in the loop.
Topology optimization for electromagnets.
Many other directions:
Other surface & curve discretizations
Multi-fidelity
Surrogates for confinement or turbulence
≥ 4D advection-dominated PDEs
Uncertainty quantification
…

## Slide 31: Extra slides

## Slide 32: A stellarator is a configuration of magnets for confining plasma without continuous rotation symmetry
Electromagnetic coils
Magnetic surfaces, plasma
Magnetic field lines
Applications: fusion energy, or electron-positron plasmas (astrophysics)
Shape of the plasma and of the coils is chosen by numerical optimization.

## Slide 33: Direct optimization of particle confinement is challenging due to computational cost & noise
Objective function to measure energy loss:
1 if particle is lost, else 0
Energy at loss time
Initial condition

## Slide 34: Divergence-free basis functions for current density J
where