## Slide 1: Efficient calculation of self-force, internal magnetic field, & stored energy for electromagnetic coils
Matt Landreman,
Siena Hurwitz,
Tom Antonsen,
University of Maryland
Notes: ~/Box/work23/20230623-01-HSX_rectangular_xsection_force_animation/20230623-01-mayavi_plot_HSX_rectangular_coil_and_force.py.gif
~/Box/work23/20230430-02-HSX_coil_force_mayavi_animation for circular-xsection version

## Slide 2: Tokamak & stellarator design requires calculations for the I x B force, internal field, and stored energy
Field and force on coil 2 due to current in coil 1 can be computed quickly: 1D filament models are ok.
Tricky part is the self-field: singularity in Biot-Savart Law
azom.com
1
2
Forces ∝ B2. High B limited by support structure.
Superconductor quench limits depend on local B.
Need to be able to dissipate stored energy W = ½LI2.
Coil shapes can probably be optimized for these quantities.

## Slide 3: Accurate calculation of the internal field and self-force appear to require high-dimensional integrals
Can we simplify/approximate these integrals for fast evaluation inside an optimization loop?
Force per unit length: 5D integral
Field: 3D integral
Self-inductance & stored energy: 6D integral
Notes: 20230501-01 Equations for coil force talk.lyx
20230717-01 Equations for coil force talk.lyx

## Slide 4: Outline
Background
Reducing 3D/5D/6D integrals to 1D/2D
Efficient quadrature for the 1D/2D integrals
Future work & conclusions

## Slide 5: Simply skipping the singular point in a 1D filament calculation gives a non-converging result with signifciant error
Maximum |B| in the conductor [Tesla]
Force per unit length [N / m]
Circular coil

## Slide 6: Analytic formulas for a circular coil show that the finite cross-section cannot be ignored
Diverges if minor radius
Could a modified 1D filament model work if we supplement it with a value for a?
Notes: 20230510-01-plot_circular_coil_mayavi
20230511-05-plot_circular_coil_mayavi_with_force_arrows

## Slide 7: Calculations of internal field and self-force are also of interest for many other subjects, e.g. solar flares
NASA/SDO/Goddard

## Slide 8: Some related work
Garren & Chen, Phys. Plasmas (1994). Looked at force but not internal field. Solution is to do a 1D integral over an incomplete loop, with a specific segment removed.
Dengler, Advanced Electromagnetics (2016). Computed self-inductance using 2D integral.
Lion, Warmer, et al Nuclear Fusion (2021). Computed B in conductor by summing analytical result for rectangular prism of J.
Robin & Volpe, Nuclear Fusion (2022). Computed force for sheet current on a winding surface.
Our contribution:
Compute self-force, stored energy / inductance, and spatially-resolved internal field using only 1D/2D integrals.
Integration is over a periodic domain, so quadrature can be spectrally accurate, & can re-use points/data from other coil optimization objectives.

## Slide 9: Outline
Background
Reducing 3D/5D/6D integrals to 1D/2D
Efficient quadrature for the 1D/2D integrals
Future work & conclusions

## Slide 10: Assumption: current density J is uniform
Ok if multiple turns in both dimensions of the x-section.
Not necessarily accurate for superconductors, particularly HTS tapes.
Good enough for optimization?
Rostila et al, (2007)
J in YBCO
current
x-sectional area
unit tangent along conductor

## Slide 11: We can do the calculations for cross-sections that are either circular or rectangular
rc
u = 1
u = -1
v = -1
v = 1
b
a
p
q
rc
a
n
b
θ
ρ
Notes: 20230717-04-mayavi_plot_HSX_circular_xsection_coil_for_coordinate_definitions
20230707-01-mayavi_plot_HSX_rectangular_coil_for_coordinate_definitions
20230511-03-plot_HSX_coil_mayavi_a1cm_incomplete.png

## Slide 12: Methodology for finding an accurate reduced model
Parameterize the coil volume:
Expansion parameter: a / R ≪ 1, where R ∼ scales of curve centerline, and b ∼ a.
Introduce intermediate scale d, with a ≪ d ≪ R.
Split integrals into “near part” + “far part”.
Far part defined by . Finite cross-section can be neglected.
Near part defined by . Coil centerline can be Taylor-expanded, so integrals can be done explicitly.
Identify a 1D integral that has the same near part and far part as the above “high fidelity” calculation for a / R ≪ 1.
centerline

## Slide 13: Methodology for finding an accurate reduced model
High fidelity 3D model
New 1D filament model
a / R ≪ 1
Far contribution:
Near contribution:

## Slide 14: Limit of the 3D integral for the internal field for a / R ≪ 1
Intuition:
Leading order near-field is same as a straight wire. But corrections contribute to the force.

## Slide 15: Our new 1D filament model reproduces the same limit as the original 3D integral
Intuition:
Regularization added to Biot-Savart. Makes a difference when source and evaluation points are as close as the coil radius.
Notes: Equations from 20230501-01_Equations_for_coil_force_talk.pdf

## Slide 16: The new filament model agrees with the high-fidelity 3D integral for B in stellarator coils
HSX coil 1
The individual B components also agree:
Notes: 20230624-01-mayavi_plot_HSX_rectangular_coil_phi0_highlight.py.png
20230621-01-HSX_rectangular_xsection_B_for_paper_hifi_modB.pdf
20230621-01-HSX_rectangular_xsection_B_for_paper_hifi_Bz.pdf
20230621-01-HSX_rectangular_xsection_B_for_paper_analytic_modB.pdf
20230621-01-HSX_rectangular_xsection_B_for_paper_analytic_Bz.pdf
CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi1_nn64_nb65_2023-05-11T10.06.03.780.dat")
CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi2_nn30_nb31_2023-04-27T09.40.25.165.dat")
20230511-02-plot_HSX_coil_with_dot_mayavi_a1cm

## Slide 17: If curve centerline is a circle, the new filament model matches analytic formula for B

## Slide 18: Integrating the J x B force over the conductor cross-section, our method reduces the 5D integral for the self-force to a 1D integral
If rc is a circle
Same as analytic result

## Slide 19: The 1D integral accurately approximates high-fidelity calculations for the self-force in stellarator coils
HSX coil 1
~ 18,000x speed-up for given precision
Notes: 20230508-01-HSX_coil_force_hifi_vs_filament.pdf
Created using CoilForces.plot_hifi_force_and_1D_for_HSX_for_talk()
3D figures created using 20230508-02-plot_HSX_coil_mayavi_a1cm
And 20230508-01-plot_HSX_coil_mayavi_a10cm
The resulting png files were opened in Preview to turn the background white into transparency.

## Slide 20: Similarly, the inductance & stored energy can be computed accurately with only a 2D integral
6D:
2D:
for circular x-section,
for rectangular x-section.
For circular centerline, matches analytic result by
Weinstein, Annalen der Physik (1884)
Notes: 20230717-01-mayavi_plot_HSX_rectangular_coil_plain_transparent.png

## Slide 21: Outline
Motivation
Reducing 3D/5D/6D integrals to 1D/2D
Efficient quadrature for the 1D/2D integrals
Future work & conclusions

## Slide 22: Remaining 1D integral is still tricky since integrand has fine structure
A solution: subtract and add a function to the integrand with the same near-singular behavior that can be integrated analytically.
With singularity subtraction
Original
Notes: plot_integrand_rectangular_xsection_for_talk()
20230717-03-mayavi_plot_HSX_rectangular_coil_phi0_highlight_ab0p02.png

## Slide 23: To make integrand smooth, we subtract and add a function with the same singular behavior that can be integrated analytically.
Compute Q by Taylor expansion of integrand about .
Result:

## Slide 24: The singularity-subtraction method allows B and the force to be evaluated with very few quadrature points.
HSX coil 1
Notes: 20230717-03-mayavi_plot_HSX_rectangular_coil_phi0_highlight_ab0p02
CoilForces.plot_force_convergence_single_for_talk()
20230511-01-HSX_force_convergence_vs_nquadpoints.pdf
20230511-02-plot_HSX_coil_with_dot_mayavi_a1cm

## Slide 25: Outline
Motivation
Reducing 3D/5D/6D integrals to 1D/2D
Efficient quadrature for the 1D/2D integrals
Future work & conclusions

## Slide 26: A possible reduced model for the critical current?
Given a model for how the local critical current density depends on B, e.g.
Gömöry and Klinčok (2006)
estimate the global critical current as
Not self-consistent, but is it good enough to be useful?
azom.com

## Slide 27: Conclusions & future work
To compute internal B field, self-force, & stored energy of a coil, the finite cross-section matters, & it is not accurate to just drop the singular point.
These quantities can be computed using just a 1D/2D integral if formulated carefully.
New method agrees with high-fidelity finite-cross-section calculations & analytic results.
Next steps:
Apply in coil optimization
Improve applicability to superconductors
Would welcome collaboration with this!

## Slide 28: Extra slides

## Slide 29: The new filament model agrees with the high-fidelity 3D integral for B in stellarator coils
HSX coil 1
|B| [T], High fidelity
|B| [T], Filament
Bz [T], High fidelity
Bz [T], Filament
The individual B components also agree:
Notes: CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi1_nn64_nb65_2023-05-11T10.06.03.780.dat")
CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi2_nn30_nb31_2023-04-27T09.40.25.165.dat")
20230511-02-plot_HSX_coil_with_dot_mayavi_a1cm

## Slide 30: The 1D integral accurately approximates high-fidelity calculations for the self-force in stellarator coils
[kN / m] for HSX coil 1, @ 150 kA
High fidelity (5D integral)
1D integral
High fidelity (5D integral)
1D integral
Parameter along curve ()
Parameter along curve ()
Notes: 20230508-01-HSX_coil_force_hifi_vs_filament.pdf
Created using CoilForces.plot_hifi_force_and_1D_for_HSX_for_talk()
3D figures created using 20230508-02-plot_HSX_coil_mayavi_a1cm
And 20230508-01-plot_HSX_coil_mayavi_a10cm
The resulting png files were opened in Preview to turn the background white into transparency.

## Slide 31: Summary of main results
Internal field:
Self-force:
Notes: 20230501-01_Equations_for_coil_force_talk.pdf