## Slide 1: How does magnetic geometry affect ITG turbulence? Insights from data & machine learning
M Landreman, J Y Choi, C Alves, P Balaprakash, R M Churchill , R Conlin, G Roberg-Clark
Thanks to many others who gave suggestions Supported by the US DOE StellFoundry SciDAC
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 2
Roberg-Clark (2022)
N = 8
Mackenbach (2022)
N = 15
Proll (2016)
N = 10
TEM proxy
This work:
N = 100,705

## Slide 3: Motivations
Profile prediction
Optimization
Understanding
Optimize geometry for maximum fusion power
Kim (2024)
Mandell (2024)
Notes: https://www.google.com/imgres?q=eureka%20understanding%20light%20bulb%20brain&imgurl=https%3A%2F%2Fpreview.redd.it%2Fhow-do-light-bulb-moments-come-about-v0-0mgno4a97tva1.jpg%3Fwidth%3D777%26format%3Dpjpg%26auto%3Dwebp%26s%3D541d28c2f1009471ab52add4a282ee4916a311fa&imgrefurl=https%3A%2F%2Fwww.reddit.com%2Fr%2Fmbti%2Fcomments%2F12xc0ef%2Fhow_do_light_bulb_moments_come_about%2F&docid=G-9kXBNk27S2YM&tbnid=9jUFrhBW814RkM&vet=12ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA..i&w=777&h=625&hcb=2&ved=2ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA

## Slide 4
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 5: Equilibria group 1: random rotating ellipses
Nfp,
aspect ratio,
elongation,
axis torsion,
and beta are all random.
All configurations have same minor radius & toroidal flux, so same gyroBohm normalization
Notes: ~/Box/work24/20241220-02-figure_of_heliiotron_equilibria$ ./20241220-02-plot_heliotron_equilibria_for_paper.py

## Slide 6: Equilibria group 2: QUASR QA & QH (Giuliani 2024)
Random pressure added for even more diversity
Notes: ~/Box/work24/20241220-01-figure_of_QUASR_equilibria$ ./20241220-01-plot_QUASR_equilibria_for_paper.py

## Slide 7: Equilibria group 3: random boundary modes
RBC and ZBS boundary Fourier modes sampled from normal distributions, fit to 44 “real” stellarators
Notes: ~/Box/work24/20241117-01-figure_of_random_equilibria$ ./20241117-02-plot_random_equilibria_for_paper.py

## Slide 8
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 9: Nonlinear turbulence simulations were run with GX in every equilibrium
Electrostatic, adiabatic electrons.
1 simulation in each tube with random dT/dx and dn/dx.
1 simulation in each tube with (a/T) dT/dx = 3, (a/n) dn/dx=0.9
8 minutes to get heat flux on 1 GPU
2×105 nonlinear simulations took < 7000 node-hours (1/8 allocation)
104
Don’t predict the time-dependence,
just the mean
Notes: This was about 1/8 of our SciDAC GPU allocation was 53,738 node hrs, UMD GPU allocation was 40,978 node hrs.
/pscratch/sd/l/landrema/20240601-01-random_stellarator_equilibria/20240601-01-075_ntheta_scan> ./plot_gx_scan_over_1_parameter_and_configuration.py
20240902-03_plot_distribution_of_Q_from_GX_database_for_poster.py
20241218-01-plot_distribution_of_heat_fluxes_for_paper.py
20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 10: Raw feature space: 7x 1D functions that enter the turbulence simulations
Flux tube simulation domain
is constant and the same for all configs, as are tube lengths in meters, so Fourier modes (kll) can be compared between configurations.
Notes: 20250127-01-plot_random_flux_tube.py

## Slide 12
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 13: Raw features should not be directly fed to classical regression or fully-connected neural network, since model should be translation-invariant
GK equation, hence heat flux, is invariant under periodic translation of the raw features in z.
Similar to computer vision, where convolutional neural networks give approximate translation-invariance.
Notes: 20250102-01-plot_geometry_for_GX_circshift_figure.py
20250102-01-plot_geometry_for_GX_circshift_animation.py
See 20240609-01 Regressions for database of GX runs.docx
/pscratch/sd/l/landrema/20240609-01-gx_convergence/20240609-01-012_circshift
plot_gx_scan_over_1_parameter_and_configuration.py
plot_Q_vs_z_vs_circshift.py
python \
/global/homes/l/landrema/gx/gx/post_processing/plot-Q-z.py \
000001_circshift_0/gx.out.nc \
000001_circshift_12/gx.out.nc \
000001_circshift_24/gx.out.nc \
000001_circshift_36/gx.out.nc \
000001_circshift_48/gx.out.nc \
000001_circshift_61/gx.out.nc \
000001_circshift_73/gx.out.nc \
000001_circshift_85/gx.out.nc

## Slide 14: Convolutional neural networks give accurate prediction of the turbulence
Convolutional layers x5
Fully connected layers x2
z-dependent geometric features
a/LT
a/Ln
Heat flux Q
Actual heat flux Q / QGB from gyrokinetic simulation
Predicted heat flux Q / QGB
R2 = 0.989
by Jong Choi, ORNL
Prediction in 0.001 sec for single network, 0.1 sec for ensemble
Notes: pred_vs_actual_plot_pre2_20250211-01-002.pdf

## Slide 15
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 16: Our interpretable models use a large library of candidate features, all translation-invariant
Start with inputs to the gyrokinetic equation & local shear:
F = {B, B-3B×∇B⋅∇y, B-2B×κ⋅∇y, B-3B×∇B⋅∇x, |∇x|², ∇x⋅∇y, |∇y|², d/dz(∇x⋅∇y / |∇x|²)}.
U = unary operations on f(z): identity, df/dz, Heaviside(f), Heaviside(-f), ReLU(f), ReLU(-f), 1/f, f2, f/B (Jacobian), f*B
C(U(F)) = U(F) and all pairwise products of functions in U(F)
Reductions: R = {min, max, max-min, mean, median, mean square, variance, skewness, L1 norm, quantiles 0.1, 0.25, 0.75, or 0.9, abs of fft coefficients 1-3, k|| with largest amplitude, expected k||, count above [-2, -1, 0, 1, 2]}
Features: R(U(C(U(F)))) > 1 million combinations

## Slide 17: Spearman correlation is a quick tool to find the most important feature
Spearman correlation is the regular Pearson correlation of the the sorted rank of the target with the sorted rank of the feature.
Its magnitude is invariant to any monotonic nonlinear function, e.g. corr(x, exp(x)) = 1
No regression model required.
Features with highest correlation to heat flux Q at fixed dT/dx & dn/dx:
Heaviside function: Where there is bad curvature,
local temperature gradient in real space (to various powers)
Jacobian (maybe squared)
Extremely similar to Mynick (2010), Xanthopoulos (2014), Stroteich (2022), Goodman (2024)!
|∇T| = (dT/dx) |∇x|

## Slide 18: Forward sequential feature selection: ∼3 features can be almost as predictive as all features
Stiffness
Critical gradient
Notes: 20241229-02-plot_sfs_results_for_talk.py

## Slide 19: Sequential feature selection allows closer fit to the data as more geometric features are included
Performance shown on 20% held-out test data
Notes: 20241224-01-plot_Q_vs_predicted_for_ML_paper.py

## Slide 20: Most important features from sequential feature selection
The gradients are more important than any geometric feature
The most important geometric feature is flux surface compression where curvature is bad
The 2nd most important geometric feature involves flux surface compression and radial ∇B drift
Classification (stability vs instability)
Regression on heat flux
Xanthopoulos et al (2011), Nakata & Matsuoka (2022):
Larger geodesic curvature (= radial drift) ⇒ Stronger damping of zonal flows ⇒ higher heat flux

## Slide 21: At each step, the top features are variations on a theme
Regression for the random-gradient dataset
Notes: 20241210-01-085_allConfigs_randomGradients_onlyUnstable_YlnQ_Qmin0p1_features20241227_XGB_20nodes

## Slide 22: Shapley values show the sign and magnitude of each feature’s effect
Decreasing importance
a/LT increases Q
a/Ln decreases Q
Shapley value: contribution to predicted ln(Q)
Most important geometric features:
|∇x| increases Q,
especially near bad curvature
Next geometric features:
Radial drift (geodesic curvature)
increases Q
Notes: 20240902-01-plot_shapley_values_for_GX_regression.py

## Slide 23: The first geometric feature can be fine-tuned for even better fit
Fixed-gradient dataset.
No regression model used here.
Feature fine-tuned for stability classifier:
Notes: 20241229-04_plot_Q_vs_optimized_single_feature_for_paper.png

## Slide 24: Previously proposed proxies can be tested
Notes: 20250206-02_compare_previously_published_ITG_proxies_singleline.py

## Slide 25: Multiple lines of evidence agree that the most important geometric feature is |∇ψ| in regions of bad curvature
Highest Spearman correlation at fixed gradients.
Consistently the first geometric feature chosen in sequential feature selection:
  In regression on the heat flux above the critical gradient
  And in the classifier for stability vs instability (i.e. determines critical gradient)
  Chosen by both XGBoost and nearest-neighbors.
Also the largest Shapley values
Notes: 20250114-06-plot_W7-X_xsection_and_surface.py

## Slide 26: There are many extensions possible
Try larger sets of possible features
From the gyrokinetic equation, understand how these features affect turbulence.
Kinetic electrons, magnetic fluctuations.
Saliency maps to understand the features learned by the neural networks.
Symbolic regression.
Kolmogorov-Arnold Networks.
Optimization, profile prediction.
Include & test other physics-motivated features.
Data will be released on Zenodo with the paper, so have a go at it!

## Slide 27
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 28: Extra slides

## Slide 29: Other machine learning regression methods work also
All using a/LT, a/Ln, and the top 10 geometric features selected via XGBoost
Notes: 20241228-01-plot_comparison_of_regression_methods.py

## Slide 30: XGBoost regression model with 1 feature
XGBoost fit
Fixed-gradient dataset
Notes: 20250128-02-plot_Q_vs_optimized_single_feature_including_xgboost.py

## Slide 31: XGBoost regression model using only a/LT and a/Ln
Same plot, showing data as dots
Notes: 20241231-03_2_feature_tprim_fprim_XGB_model_visualization.ipynb

## Slide 32: XGBoost regression model for fixed gradients using 2 features
Same plot, showing data as dots
Notes: 20241231-02_2_feature_XGB_model_visualization.ipynb