## Slide 1: How does magnetic geometry affect ITG turbulence? Insights from data & machine learning
M Landreman, J Y Choi, C Alves, P Balaprakash, R M Churchill , R Conlin, G Roberg-Clark arXiv:2502.11657
Thanks to many others who gave suggestions Supported by the US DOE StellFoundry SciDAC
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 2: Motivations
Profile prediction
Optimization
Understanding
Mandell (2024)
Kim (2024)
Notes: https://www.google.com/imgres?q=eureka%20understanding%20light%20bulb%20brain&imgurl=https%3A%2F%2Fpreview.redd.it%2Fhow-do-light-bulb-moments-come-about-v0-0mgno4a97tva1.jpg%3Fwidth%3D777%26format%3Dpjpg%26auto%3Dwebp%26s%3D541d28c2f1009471ab52add4a282ee4916a311fa&imgrefurl=https%3A%2F%2Fwww.reddit.com%2Fr%2Fmbti%2Fcomments%2F12xc0ef%2Fhow_do_light_bulb_moments_come_about%2F&docid=G-9kXBNk27S2YM&tbnid=9jUFrhBW814RkM&vet=12ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA..i&w=777&h=625&hcb=2&ved=2ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA

## Slide 3
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 4: Equilibria include rotating ellipses, quasi-symmetric, and random shapes
Aspect ratio,
elongation, q = 1 / ι, β, and number of field periods are all varied.
All configurations scaled to have same gyroBohm normalizations
(Tokamak generation underway by Ralf Mackenbach)
Notes: ~/Box/work24/20241220-02-figure_of_heliiotron_equilibria$ ./20241220-02-plot_heliotron_equilibria_for_paper.py

## Slide 5: Nonlinear turbulence simulations were run with GX in every equilibrium
Electrostatic, adiabatic electrons.
1 simulation in each tube with random dT/dx and dn/dx.
1 simulation in each tube with (a/T) dT/dx = 3, (a/n) dn/dx=0.9
8 minutes to get heat flux on 1 GPU
2×105 nonlinear simulations took < 7000 node-hours
104
Notes: This was about 1/8 of our SciDAC GPU allocation was 53,738 node hrs, UMD GPU allocation was 40,978 node hrs.
/pscratch/sd/l/landrema/20240601-01-random_stellarator_equilibria/20240601-01-075_ntheta_scan> ./plot_gx_scan_over_1_parameter_and_configuration.py
20240902-03_plot_distribution_of_Q_from_GX_database_for_poster.py
20241218-01-plot_distribution_of_heat_fluxes_for_paper.py
20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 6
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 7: Raw feature space: 7x 1D functions that enter the turbulence simulations
Flux tube simulation domain
is constant and the same for all configs, as are tube lengths in meters, so Fourier modes (kll) can be compared between configurations.
Notes: 20250127-01-plot_random_flux_tube.py

## Slide 8: Raw features should not be directly fed to classical regression or fully-connected neural network, since model should be translation-invariant
GK equation, hence heat flux, is invariant under periodic translation of the raw features in z.
Similar to computer vision, where convolutional neural networks give approximate translation-invariance.
Notes: 20250102-01-plot_geometry_for_GX_circshift_figure.py
20250102-01-plot_geometry_for_GX_circshift_animation.py
See 20240609-01 Regressions for database of GX runs.docx
/pscratch/sd/l/landrema/20240609-01-gx_convergence/20240609-01-012_circshift
plot_gx_scan_over_1_parameter_and_configuration.py
plot_Q_vs_z_vs_circshift.py
python \
/global/homes/l/landrema/gx/gx/post_processing/plot-Q-z.py \
000001_circshift_0/gx.out.nc \
000001_circshift_12/gx.out.nc \
000001_circshift_24/gx.out.nc \
000001_circshift_36/gx.out.nc \
000001_circshift_48/gx.out.nc \
000001_circshift_61/gx.out.nc \
000001_circshift_73/gx.out.nc \
000001_circshift_85/gx.out.nc

## Slide 9: Convolutional neural networks give accurate prediction of the turbulence
Convolutional layers x5
Fully connected layers x2
z-dependent geometric features
a/LT
a/Ln
Heat flux Q
Actual heat flux Q / QGB from gyrokinetic simulation
Predicted heat flux Q / QGB
R2 = 0.989
by Jong Choi, ORNL
Prediction in 0.001 sec for single network, 0.1 sec for ensemble
Notes: pred_vs_actual_plot_pre2_20250211-01-002.pdf

## Slide 10
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Spearman correlation
Sequential feature selection
Shapley values
Testing physics-based surrogates
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 11: Our interpretable models use a large library of candidate features, all translation-invariant
Start with inputs to the gyrokinetic equation & local shear:
B, B-3B×∇B⋅∇y, B-2B×κ⋅∇y, B-3B×∇B⋅∇x,
|∇x|², ∇x⋅∇y, |∇y|², d/dz(∇x⋅∇y / |∇x|²).
Apply unary operations on f(z): f2, df/dz, Heaviside(f), etc.,
Include all pairwise products,
Reductions: max, median, abs of fft coefficients, k|| with largest amplitude, etc.
> 1 million combinations

## Slide 12: Spearman correlation is a quick tool to find the most important feature
Unlike Pearson, Spearman is invariant to any monotonic function.
Features with highest correlation to heat flux Q at fixed dT/dx & dn/dx:
Heaviside function: Where there is bad curvature,
local temperature gradient in real space (to various powers)
Jacobian (maybe squared)
Extremely similar to Mynick (2010), Xanthopoulos (2014), Stroteich (2022), Goodman (2024)!
|∇T| = (dT/dx) |∇x|
?!?! |∇x| does not appear in gyrokinetic equation for kx = 0 modes!
Notes: 20250114-06-plot_W7-X_xsection_and_surface.py

## Slide 13: Another method to identify most important features: forward sequential feature selection
Stiffness
Critical gradient
Using decision trees (XGBoost library), varied-gradient dataset
Notes: 20241229-07-plot_sfs_results_for_talk_simplified.py

## Slide 14: Most important features from sequential feature selection
The gradients are more important than any geometric feature
The most important geometric feature is flux surface compression where curvature is bad
The 2nd most important geometric feature involves flux surface compression and radial ∇B drift
Classification (stability vs instability)
Regression on heat flux
Xanthopoulos et al (2011), Nakata & Matsuoka (2022):
Larger geodesic curvature (= radial drift) ⇒ Stronger damping of zonal flows ⇒ higher heat flux

## Slide 15: Shapley values show the sign and magnitude of each feature’s effect
Decreasing importance
a/LT increases Q
a/Ln decreases Q
Shapley value: contribution to predicted ln(Q)
Most important geometric features:
|∇x| increases Q,
especially near bad curvature
Next geometric features:
Radial drift (geodesic curvature)
increases Q
Notes: 20240902-01-plot_shapley_values_for_GX_regression.py

## Slide 16: Previously proposed proxies can be tested
Notes: 20250206-02_compare_previously_published_ITG_proxies_singleline.py

## Slide 17: Summary
From the gyrokinetic equation, understand how top features affect turbulence.
Saliency maps to understand the features learned by the neural networks.
Other interpretable methods (symbolic regression, Kolmogorov-Arnold Networks)
Kinetic electrons, magnetic fluctuations.
Optimization & profile prediction.
Future work
Interpretable ML can reveal trends and stimulate theory.
Most important feature for ITG seems to be |∇ψ| in regions of bad curvature.
Paper:
arXiv:2502.11657
Dataset
doi:10.5281/zenodo.14867776

## Slide 18: Extra slides

## Slide 19
Roberg-Clark (2022)
N = 8
Mackenbach (2022)
N = 15
Proll (2016)
N = 10
TEM proxy
This work:
N = 100,705

## Slide 20: Motivations
Profile prediction
Optimization
Understanding
Optimize geometry for maximum fusion power
Kim (2024)
Mandell (2024)
Notes: https://www.google.com/imgres?q=eureka%20understanding%20light%20bulb%20brain&imgurl=https%3A%2F%2Fpreview.redd.it%2Fhow-do-light-bulb-moments-come-about-v0-0mgno4a97tva1.jpg%3Fwidth%3D777%26format%3Dpjpg%26auto%3Dwebp%26s%3D541d28c2f1009471ab52add4a282ee4916a311fa&imgrefurl=https%3A%2F%2Fwww.reddit.com%2Fr%2Fmbti%2Fcomments%2F12xc0ef%2Fhow_do_light_bulb_moments_come_about%2F&docid=G-9kXBNk27S2YM&tbnid=9jUFrhBW814RkM&vet=12ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA..i&w=777&h=625&hcb=2&ved=2ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA

## Slide 21
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 22: Equilibria group 1: random rotating ellipses
Nfp,
aspect ratio,
elongation,
axis torsion,
and beta are all random.
All configurations have same minor radius & toroidal flux, so same gyroBohm normalization
Notes: ~/Box/work24/20241220-02-figure_of_heliiotron_equilibria$ ./20241220-02-plot_heliotron_equilibria_for_paper.py

## Slide 23: Equilibria group 2: QUASR QA & QH (Giuliani 2024)
Random pressure added for even more diversity
Notes: ~/Box/work24/20241220-01-figure_of_QUASR_equilibria$ ./20241220-01-plot_QUASR_equilibria_for_paper.py

## Slide 24: Equilibria group 3: random boundary modes
RBC and ZBS boundary Fourier modes sampled from normal distributions, fit to 44 “real” stellarators
Notes: ~/Box/work24/20241117-01-figure_of_random_equilibria$ ./20241117-02-plot_random_equilibria_for_paper.py

## Slide 26: Our interpretable models use a large library of candidate features, all translation-invariant
Start with inputs to the gyrokinetic equation & local shear:
F = {B, B-3B×∇B⋅∇y, B-2B×κ⋅∇y, B-3B×∇B⋅∇x, |∇x|², ∇x⋅∇y, |∇y|², d/dz(∇x⋅∇y / |∇x|²)}.
U = unary operations on f(z): identity, df/dz, Heaviside(f), Heaviside(-f), ReLU(f), ReLU(-f), 1/f, f2, f/B (Jacobian), f*B
C(U(F)) = U(F) and all pairwise products of functions in U(F)
Reductions: R = {min, max, max-min, mean, median, mean square, variance, skewness, L1 norm, quantiles 0.1, 0.25, 0.75, or 0.9, abs of fft coefficients 1-3, k|| with largest amplitude, expected k||, count above [-2, -1, 0, 1, 2]}
Features: R(U(C(U(F)))) > 1 million combinations

## Slide 27: Spearman correlation is a quick tool to find the most important feature
Spearman correlation is the regular Pearson correlation of the the sorted rank of the target with the sorted rank of the feature.
Its magnitude is invariant to any monotonic nonlinear function, e.g. corr(x, exp(x)) = 1
No regression model required.
Features with highest correlation to heat flux Q at fixed dT/dx & dn/dx:
Heaviside function: Where there is bad curvature,
local temperature gradient in real space (to various powers)
Jacobian (maybe squared)
Extremely similar to Mynick (2010), Xanthopoulos (2014), Stroteich (2022), Goodman (2024)!
|∇T| = (dT/dx) |∇x|

## Slide 28: Forward sequential feature selection: ∼3 features can be almost as predictive as all features
Stiffness
Critical gradient
Notes: 20241229-02-plot_sfs_results_for_talk.py

## Slide 29: Sequential feature selection allows closer fit to the data as more geometric features are included
Performance shown on 20% held-out test data
Notes: 20241224-01-plot_Q_vs_predicted_for_ML_paper.py

## Slide 30: At each step, the top features are variations on a theme
Regression for the random-gradient dataset
Notes: 20241210-01-085_allConfigs_randomGradients_onlyUnstable_YlnQ_Qmin0p1_features20241227_XGB_20nodes

## Slide 31: Other machine learning regression methods work also
All using a/LT, a/Ln, and the top 10 geometric features selected via XGBoost
Notes: 20241228-01-plot_comparison_of_regression_methods.py

## Slide 32: The first geometric feature can be fine-tuned for even better fit
Fixed-gradient dataset.
No regression model used here.
Feature fine-tuned for stability classifier:
Notes: 20241229-04_plot_Q_vs_optimized_single_feature_for_paper.png

## Slide 33: XGBoost regression model with 1 feature
XGBoost fit
Fixed-gradient dataset
Notes: 20250128-02-plot_Q_vs_optimized_single_feature_including_xgboost.py

## Slide 34: XGBoost regression model using only a/LT and a/Ln
Same plot, showing data as dots
Notes: 20241231-03_2_feature_tprim_fprim_XGB_model_visualization.ipynb

## Slide 35: XGBoost regression model for fixed gradients using 2 features
Same plot, showing data as dots
Notes: 20241231-02_2_feature_XGB_model_visualization.ipynb

## Slide 36
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 37: Multiple lines of evidence agree that the most important geometric feature is |∇ψ| in regions of bad curvature
Highest Spearman correlation at fixed gradients.
Consistently the first geometric feature chosen in sequential feature selection:
  In regression on the heat flux above the critical gradient
  And in the classifier for stability vs instability (i.e. determines critical gradient)
  Chosen by XGBoost, nearest-neighbors, & other algorithms.
Also the largest Shapley values
Notes: 20250114-06-plot_W7-X_xsection_and_surface.py

## Slide 38: There are many extensions possible
Try larger sets of possible features
From the gyrokinetic equation, understand how these features affect turbulence.
Kinetic electrons, magnetic fluctuations.
Saliency maps to understand the features learned by the neural networks.
Symbolic regression.
Kolmogorov-Arnold Networks.
Optimization, profile prediction.
Include & test other physics-motivated features.
Data is online at doi:10.5281/zenodo.14867776, so have a go at it!

## Slide 39
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Paper: arXiv:2502.11657 Dataset doi:10.5281/zenodo.14867776
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 40
Notes: 20250321-01_compare_variants_of_ITG_proxy_grad_x_vs_grad_y.pdf