## Slide 1: Efficient interpretable regression and classification with translation-invariance
M Landreman, J Y Choi, C Alves, P Balaprakash, R M Churchill , R Conlin, G Roberg-Clark
Journal of Plasma Physics 91, E120 (2025), arXiv:2502.11657
Regression,
classification
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 2: Efficient interpretable regression and classification with translation-invariance
Motivating application: turbulence in fusion plasmas
Regression/classification method
Results

## Slide 3: Efficient interpretable regression and classification with translation-invariance
Motivating application: turbulence in fusion plasmas
Regression/classification method
Results

## Slide 4
Chart from Fusion Industry Association

## Slide 5: Turbulence in fusion plasmas: we want to understand & optimize
Gradients of plasma density & temperature cause instabilities & turbulence.
Causes heat to leak out.
Known to depend on plasma shape, but how exactly?
Geometry could be optimized to reduce turbulence
Turbulence simulations: ~10 GPU-min to 106s of CPU-hours.
5D + time
Nunami 2012
Electrostatic potential
Notes: Turbulence image from http://fusionsites.ciemat.es/gyrokineticsmadrid2014/files/2014/06/Nunami.pdf
From https://aip.scitation.org/doi/pdf/10.1063/1.4704568 Nunami et al., PoP 19, 042504 (2012)

## Slide 6: Turbulence in fusion plasmas is highly anisotropic due to magnetic field
Nunami 2012
Electrostatic potential
Magnetic field line
Particle trajectory
Notes: Turbulence image from http://fusionsites.ciemat.es/gyrokineticsmadrid2014/files/2014/06/Nunami.pdf
From https://aip.scitation.org/doi/pdf/10.1063/1.4704568 Nunami et al., PoP 19, 042504 (2012)

## Slide 7: Approach here: learn how turbulence depends on geometry using data
Start with direct numerical simulations of turbulence in 105 geometries
“Flux tube” simulation domain
z
y
x
Notes: ~/Box/work24/20241220-02-figure_of_heliiotron_equilibria$ ./20241220-02-plot_heliotron_equilibria_for_paper.py

## Slide 8: Equations describing the turbulence
Electrostatic potential:
Ion distribution function:
Gyrokinetic equation:
Quasineutrality:
Heat flux:
Notes: 20250821-01_Equations_for_numerical_analysis_seminar_on_gyrokinetic_equation.lyx

## Slide 9: Nonlinear turbulence simulations were run in 105 geometries
1 simulation in each tube with random dT/dx and dn/dx.
1 simulation in each tube with (a/T) dT/dx = 3, (a/n) dn/dx=0.9
8 minutes to get heat flux on 1 GPU
2×105 nonlinear simulations took < 7000 node-hours
104
Notes: This was about 1/8 of our SciDAC GPU allocation was 53,738 node hrs, UMD GPU allocation was 40,978 node hrs.
/pscratch/sd/l/landrema/20240601-01-random_stellarator_equilibria/20240601-01-075_ntheta_scan> ./plot_gx_scan_over_1_parameter_and_configuration.py
20240902-03_plot_distribution_of_Q_from_GX_database_for_poster.py
20241218-01-plot_distribution_of_heat_fluxes_for_paper.py
20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 10: Raw feature space: 7x 1D functions that enter the turbulence simulations
Flux tube simulation domain
z
y
x
Notes: 20250127-01-plot_random_flux_tube.py

## Slide 11: Raw features should not be directly fed to classical regression or fully-connected neural network, since model should be translation-invariant
Gyrokinetic equation, hence heat flux, is invariant under periodic translation of the raw features in z.
Similar to computer vision, where convolutional neural networks give approximate translation-invariance.
Notes: 20250102-01-plot_geometry_for_GX_circshift_figure.py
20250102-01-plot_geometry_for_GX_circshift_animation.py
See 20240609-01 Regressions for database of GX runs.docx
/pscratch/sd/l/landrema/20240609-01-gx_convergence/20240609-01-012_circshift
plot_gx_scan_over_1_parameter_and_configuration.py
plot_Q_vs_z_vs_circshift.py
python \
/global/homes/l/landrema/gx/gx/post_processing/plot-Q-z.py \
000001_circshift_0/gx.out.nc \
000001_circshift_12/gx.out.nc \
000001_circshift_24/gx.out.nc \
000001_circshift_36/gx.out.nc \
000001_circshift_48/gx.out.nc \
000001_circshift_61/gx.out.nc \
000001_circshift_73/gx.out.nc \
000001_circshift_85/gx.out.nc

## Slide 12: Efficient interpretable regression and classification with translation-invariance
Motivating application: turbulence in fusion plasmas
Regression/classification method
Results

## Slide 13: Convolutional neural networks give accurate prediction of the turbulence, but lack interpretability
Convolutional layers x5
Fully connected layers x2
z-dependent geometric features
a/LT
a/Ln
Heat flux Q
Actual heat flux Q / QGB from gyrokinetic simulation
Predicted heat flux Q / QGB
R2 = 0.989
Notes: pred_vs_actual_plot_pre2_20250211-01-002.pdf

## Slide 14: Regression/classification method to achieve invariance & interpretability
Define library of candidate features which are all translation-invariant. (Akin to SINDy).
Apply a fast regression/classification method like decision trees to these features.
Use forward sequential feature selection to pick out only the most important features.
Guarantees that model will respect the invariance.
Each feature is an analytic expression ⇒ partially interpretable.
Step 2 allows extra nonlinearity beyond functions in the library.
Method in step 2 must be fast to fit because we will fit millions of models.

## Slide 15: To create library of candidate features, apply any translation-invariant reduction to translation-equivariant operations
Invariance
Equivariance
Figure by Bernhard Kainz
Notes: https://www.doc.ic.ac.uk/~bkainz/teaching/DL/notes/equivariance.pdf

## Slide 16: To create library of candidate features, apply any translation-invariant reduction to translation-equivariant operations
Start with inputs to the gyrokinetic equation:
F = {B, B-3B×∇B⋅∇y, B-2B×κ⋅∇y, B-3B×∇B⋅∇x, |∇x|², ∇x⋅∇y, |∇y|²}.
U = unary operations on f(z): identity, df/dz, Heaviside(f), Heaviside(-f), ReLU(f), ReLU(-f), 1/f, f2, f/B (Jacobian), f*B
C(U(F)) = U(F) and all pairwise products of functions in U(F)
Reductions: R = {min, max, max-min, mean, median, mean square, variance, skewness, L1 norm, quantiles 0.1, 0.25, 0.75, or 0.9, abs of fft coefficients 1-3, k|| with largest amplitude, expected k||, count above [-2, -1, 0, 1, 2]}
Features: R(U(C(U(F)))) > 1 million combinations

## Slide 17: Efficient interpretable regression and classification with translation-invariance
Motivating application: turbulence in fusion plasmas
Regression/classification method
Results

## Slide 18: Forward sequential feature selection
Using decision trees (XGBoost library), varied-gradient dataset
Notes: 20241229-07-plot_sfs_results_for_talk_simplified.py

## Slide 19: Most important features from sequential feature selection
The gradients are more important than any geometric feature
Classification (stability vs instability)
Regression on heat flux
Xanthopoulos et al (2011), Nakata & Matsuoka (2022):
Larger geodesic curvature (= radial drift) ⇒ Stronger damping of zonal flows ⇒ higher heat flux
Most important geometric feature:
Local temperature gradient in real space |∇T| = (dT/dx) |∇x|, where there is bad curvature.
Similar to proposed physics-inspired surrogates
[Mynick (2010), Xanthopoulos (2014), Stroteich (2022), Goodman (2024)].

## Slide 20: Sequential feature selection allows closer fit to the data as more geometric features are included
Performance shown on 20% held-out test data
Notes: 20241224-01-plot_Q_vs_predicted_for_ML_paper.py

## Slide 21: The first geometric feature can be fine-tuned for even better fit
Notes: 20241229-04_plot_Q_vs_optimized_single_feature_for_paper.png

## Slide 22: Summary
Use model for optimizing geometry & predicting temperature.
Compare to saliency maps for the neural networks.
Include physics-motivated features (e.g. linear growth rates).
Generate data with higher physics fidelity, repeat analysis.
Other suggestions for methods to try?
Future work
Interpretable regression/classification guaranteeing translation-invariance.
Library of candidate invariant features + decision trees + feature selection.
Most important features align with recent physics-motivated surrogates.
Journal of Plasma Physics 91, E120 (2025)
arXiv:2502.11657

## Slide 23: Extra slides

## Slide 24: How does magnetic geometry affect ITG turbulence? Insights from data & machine learning
M Landreman, J Y Choi, C Alves, P Balaprakash, R M Churchill , R Conlin, G Roberg-Clark arXiv:2502.11657
Thanks to many others who gave suggestions Supported by the US DOE StellFoundry SciDAC
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 25
Roberg-Clark (2022)
N = 8
Mackenbach (2022)
N = 15
Proll (2016)
N = 10
TEM proxy
This work:
N = 100,705

## Slide 26: Motivations
Profile prediction
Optimization
Understanding
Optimize geometry for maximum fusion power
Kim (2024)
Mandell (2024)
Notes: https://www.google.com/imgres?q=eureka%20understanding%20light%20bulb%20brain&imgurl=https%3A%2F%2Fpreview.redd.it%2Fhow-do-light-bulb-moments-come-about-v0-0mgno4a97tva1.jpg%3Fwidth%3D777%26format%3Dpjpg%26auto%3Dwebp%26s%3D541d28c2f1009471ab52add4a282ee4916a311fa&imgrefurl=https%3A%2F%2Fwww.reddit.com%2Fr%2Fmbti%2Fcomments%2F12xc0ef%2Fhow_do_light_bulb_moments_come_about%2F&docid=G-9kXBNk27S2YM&tbnid=9jUFrhBW814RkM&vet=12ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA..i&w=777&h=625&hcb=2&ved=2ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA

## Slide 27: Motivations
Profile prediction
Optimization
Understanding
Mandell (2024)
Kim (2024)
Notes: https://www.google.com/imgres?q=eureka%20understanding%20light%20bulb%20brain&imgurl=https%3A%2F%2Fpreview.redd.it%2Fhow-do-light-bulb-moments-come-about-v0-0mgno4a97tva1.jpg%3Fwidth%3D777%26format%3Dpjpg%26auto%3Dwebp%26s%3D541d28c2f1009471ab52add4a282ee4916a311fa&imgrefurl=https%3A%2F%2Fwww.reddit.com%2Fr%2Fmbti%2Fcomments%2F12xc0ef%2Fhow_do_light_bulb_moments_come_about%2F&docid=G-9kXBNk27S2YM&tbnid=9jUFrhBW814RkM&vet=12ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA..i&w=777&h=625&hcb=2&ved=2ahUKEwjdq_HN6OOKAxW7MVkFHflMNswQM3oECHAQAA

## Slide 28
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 29: Equilibria include rotating ellipses, quasi-symmetric, and random shapes
Aspect ratio,
elongation, q = 1 / ι, β, and number of field periods are all varied.
All configurations scaled to have same gyroBohm normalizations
(Tokamak generation underway by Ralf Mackenbach)
Notes: ~/Box/work24/20241220-02-figure_of_heliiotron_equilibria$ ./20241220-02-plot_heliotron_equilibria_for_paper.py

## Slide 30
Regression
Turbulence simulations
Feature importance
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 31: Equilibria group 1: random rotating ellipses
Nfp,
aspect ratio,
elongation,
axis torsion,
and beta are all random.
All configurations have same minor radius & toroidal flux, so same gyroBohm normalization
Notes: ~/Box/work24/20241220-02-figure_of_heliiotron_equilibria$ ./20241220-02-plot_heliotron_equilibria_for_paper.py

## Slide 32: Equilibria group 2: QUASR QA & QH (Giuliani 2024)
Random pressure added for even more diversity
Notes: ~/Box/work24/20241220-01-figure_of_QUASR_equilibria$ ./20241220-01-plot_QUASR_equilibria_for_paper.py

## Slide 33: Equilibria group 3: random boundary modes
RBC and ZBS boundary Fourier modes sampled from normal distributions, fit to 44 “real” stellarators
Notes: ~/Box/work24/20241117-01-figure_of_random_equilibria$ ./20241117-02-plot_random_equilibria_for_paper.py

## Slide 35: Our interpretable models use a large library of candidate features, all translation-invariant
Start with inputs to the gyrokinetic equation & local shear:
F = {B, B-3B×∇B⋅∇y, B-2B×κ⋅∇y, B-3B×∇B⋅∇x, |∇x|², ∇x⋅∇y, |∇y|², d/dz(∇x⋅∇y / |∇x|²)}.
U = unary operations on f(z): identity, df/dz, Heaviside(f), Heaviside(-f), ReLU(f), ReLU(-f), 1/f, f2, f/B (Jacobian), f*B
C(U(F)) = U(F) and all pairwise products of functions in U(F)
Reductions: R = {min, max, max-min, mean, median, mean square, variance, skewness, L1 norm, quantiles 0.1, 0.25, 0.75, or 0.9, abs of fft coefficients 1-3, k|| with largest amplitude, expected k||, count above [-2, -1, 0, 1, 2]}
Features: R(U(C(U(F)))) > 1 million combinations

## Slide 36: Spearman correlation is a quick tool to find the most important feature
Spearman correlation is the regular Pearson correlation of the the sorted rank of the target with the sorted rank of the feature.
Its magnitude is invariant to any monotonic nonlinear function, e.g. corr(x, exp(x)) = 1
No regression model required.
Features with highest correlation to heat flux Q at fixed dT/dx & dn/dx:
Heaviside function: Where there is bad curvature,
local temperature gradient in real space (to various powers)
Jacobian (maybe squared)
Extremely similar to Mynick (2010), Xanthopoulos (2014), Stroteich (2022), Goodman (2024)!
|∇T| = (dT/dx) |∇x|

## Slide 37: Forward sequential feature selection: ∼3 features can be almost as predictive as all features
Stiffness
Critical gradient
Notes: 20241229-02-plot_sfs_results_for_talk.py

## Slide 38: Sequential feature selection allows closer fit to the data as more geometric features are included
Performance shown on 20% held-out test data
Notes: 20241224-01-plot_Q_vs_predicted_for_ML_paper.py

## Slide 39: At each step, the top features are variations on a theme
Regression for the random-gradient dataset
Notes: 20241210-01-085_allConfigs_randomGradients_onlyUnstable_YlnQ_Qmin0p1_features20241227_XGB_20nodes

## Slide 40: Spearman correlation is a quick tool to find the most important feature
Unlike Pearson, Spearman is invariant to any monotonic function.
Features with highest correlation to heat flux Q at fixed dT/dx & dn/dx:
Heaviside function: Where there is bad curvature,
local temperature gradient in real space (to various powers)
Jacobian (maybe squared)
Extremely similar to Mynick (2010), Xanthopoulos (2014), Stroteich (2022), Goodman (2024)!
|∇T| = (dT/dx) |∇x|
Notes: 20250114-06-plot_W7-X_xsection_and_surface.py

## Slide 41: Previously proposed proxies can be tested
Notes: 20250206-02_compare_previously_published_ITG_proxies_singleline.py

## Slide 42: Other machine learning regression methods work also
All using a/LT, a/Ln, and the top 10 geometric features selected via XGBoost
Notes: 20241228-01-plot_comparison_of_regression_methods.py

## Slide 43: XGBoost regression model with 1 feature
XGBoost fit
Fixed-gradient dataset
Notes: 20250128-02-plot_Q_vs_optimized_single_feature_including_xgboost.py

## Slide 44: XGBoost regression model using only a/LT and a/Ln
Same plot, showing data as dots
Notes: 20241231-03_2_feature_tprim_fprim_XGB_model_visualization.ipynb

## Slide 45: XGBoost regression model for fixed gradients using 2 features
Same plot, showing data as dots
Notes: 20241231-02_2_feature_XGB_model_visualization.ipynb

## Slide 46
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 47: Multiple lines of evidence agree that the most important geometric feature is |∇ψ| in regions of bad curvature
Highest Spearman correlation at fixed gradients.
Consistently the first geometric feature chosen in sequential feature selection:
  In regression on the heat flux above the critical gradient
  And in the classifier for stability vs instability (i.e. determines critical gradient)
  Chosen by XGBoost, nearest-neighbors, & other algorithms.
Also the largest Shapley values
Notes: 20250114-06-plot_W7-X_xsection_and_surface.py

## Slide 48: There are many extensions possible
Try larger sets of possible features
From the gyrokinetic equation, understand how these features affect turbulence.
Kinetic electrons, magnetic fluctuations.
Saliency maps to understand the features learned by the neural networks.
Symbolic regression.
Kolmogorov-Arnold Networks.
Optimization, profile prediction.
Include & test other physics-motivated features.
Data is online at doi:10.5281/zenodo.14867776, so have a go at it!

## Slide 49
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Paper: arXiv:2502.11657 Dataset doi:10.5281/zenodo.14867776
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 50
Turbulence simulations
Feature importance
Regression
True heat flux
Predicted heat flux
R2 = 0.989
Notes: 20250102-10_plot_Q_vs_time_for_several_simulations.pdf

## Slide 51: To create library of candidate features, apply any translation-invariant reduction to translation-equivariant operations
Start with inputs to the gyrokinetic equation & local shear:
B, B-3B×∇B⋅∇y, B-2B×κ⋅∇y, B-3B×∇B⋅∇x,
|∇x|², ∇x⋅∇y, |∇y|², d/dz(∇x⋅∇y / |∇x|²).
Apply unary operations on f(z): f2, df/dz, Heaviside(f), etc.,
Include all pairwise products,
Reductions: max, median, abs of fft coefficients, k|| with largest amplitude, etc.
> 1 million combinations

## Slide 52: Most important features from sequential feature selection
The gradients are more important than any geometric feature
The most important geometric feature is flux surface compression where curvature is bad
The 2nd most important geometric feature involves flux surface compression and radial ∇B drift
Classification (stability vs instability)
Regression on heat flux
Xanthopoulos et al (2011), Nakata & Matsuoka (2022):
Larger geodesic curvature (= radial drift) ⇒ Stronger damping of zonal flows ⇒ higher heat flux

## Slide 53: Shapley values show the sign and magnitude of each feature’s effect
Decreasing importance
a/LT increases Q
a/Ln decreases Q
Shapley value: contribution to predicted ln(Q)
Most important geometric features:
|∇x| increases Q,
especially near bad curvature
Next geometric features:
Radial drift (geodesic curvature)
increases Q
Notes: 20240902-01-plot_shapley_values_for_GX_regression.py

## Slide 54: Summary
From the gyrokinetic equation, understand how top features affect turbulence.
Saliency maps to understand the features learned by the neural networks.
Other interpretable methods (symbolic regression, Kolmogorov-Arnold Networks)
Kinetic electrons, magnetic fluctuations.
Optimization & profile prediction.
Future work
Interpretable ML can reveal trends and stimulate theory.
Most important feature for ITG seems to be |∇ψ| in regions of bad curvature.
Paper:
arXiv:2502.11657
Dataset
doi:10.5281/zenodo.14867776

## Slide 55
Notes: 20250321-01_compare_variants_of_ITG_proxy_grad_x_vs_grad_y.pdf