## Slide 1: Some theoretical advances for easing stellarator power plant engineering challenges
Matt Landreman1, John Kappel1, Siena Hurwitz1, Tom Antonsen1, Dhairya Malhotra2,
1. Maryland 2. Flatiron Institute
1. Reduced model for coil self-field, self-force, & critical current
arXiv:2310.09313, arXiv:2310.12087
2. Room for a blanket, & understanding coil-plasma distance
arXiv:2309.11342
Supported by DOE DE-FG02-93ER54197 & the Simons Foundation 560651
Notes: 11 min + 2 for questions
~/Box/work23/20230623-01-HSX_rectangular_xsection_force_animation/20230623-01-mayavi_plot_HSX_rectangular_coil_and_force.py.gif
~/Box/work23/20230430-02-HSX_coil_force_mayavi_animation for circular-xsection version

## Slide 2: Motivation: We’d like to quickly evaluate & optimize I x B forces, internal field, and stored energy
Forces ∝ B2. High B limited by support structure.
Superconductor quench limits depend on local B.
Need to be able to dissipate stored energy W = ½LI2.
Tricky part is the self-field: singularity in Biot-Savart Law
Circular coil
Diverges if minor radius

## Slide 3: Methodology for finding an accurate reduced model
rc
b
a
rc
a
Introduce intermediate scale d, with a ∼ b ≪ d ≪ R (scale of curve center-line rc.)
Split Biot-Savart integrals into “near part” (, Taylor-expand) + “far part” (, neglect finite thickness)
Identify a 1D integral that has the same near part and far part as the above “high fidelity” calculation for a / R ≪ 1.

## Slide 4: New 1D integral accurately approximates high-fidelity calculations for the self-force in stellarator coils
HSX coil 1
~ 18,000x speed-up for given precision
Model also reproduces high-fidelity calculations for self-inductance & stored energy.
for circular x-section, more complicated for rectangular x-section.
Notes: 20230717-01 Equations for coil force talk.lyx
20230508-01-HSX_coil_force_hifi_vs_filament.pdf
Created using CoilForces.plot_hifi_force_and_1D_for_HSX_for_talk()
3D figures created using 20230508-02-plot_HSX_coil_mayavi_a1cm
And 20230508-01-plot_HSX_coil_mayavi_a10cm
The resulting png files were opened in Preview to turn the background white into transparency.

## Slide 5: Similar 1D integral for B agrees with the high-fidelity 3D integral for B in stellarator coils
HSX coil 1
The individual B components also agree:
Estimate critical current by iterating with
Gömöry and Klinčok (2006)
?
Notes: 20230624-01-mayavi_plot_HSX_rectangular_coil_phi0_highlight.py.png
20230621-01-HSX_rectangular_xsection_B_for_paper_hifi_modB.pdf
20230621-01-HSX_rectangular_xsection_B_for_paper_hifi_Bz.pdf
20230621-01-HSX_rectangular_xsection_B_for_paper_analytic_modB.pdf
20230621-01-HSX_rectangular_xsection_B_for_paper_analytic_Bz.pdf
CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi1_nn64_nb65_2023-05-11T10.06.03.780.dat")
CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi2_nn30_nb31_2023-04-27T09.40.25.165.dat")
20230511-02-plot_HSX_coil_with_dot_mayavi_a1cm

## Slide 6: Some theoretical advances for easing stellarator power plant engineering challenges
1. Reduced model for coil self-field, self-force, & critical current
arXiv:2310.09313, arXiv:2310.12087
2. Room for a blanket, & understanding coil-plasma distance
arXiv:2309.11342
Supported by DOE DE-FG02-93ER54197 & the Simons Foundation 560651
Matt Landreman1, John Kappel1, Siena Hurwitz1, Tom Antonsen1, Dhairya Malhotra2,
1. Maryland 2. Flatiron Institute
Notes: 11 min + 2 for questions
~/Box/work23/20230623-01-HSX_rectangular_xsection_force_animation/20230623-01-mayavi_plot_HSX_rectangular_coil_and_force.py.gif
~/Box/work23/20230430-02-HSX_coil_force_mayavi_animation for circular-xsection version

## Slide 7: In a reactor, must fit ~ 1.5m “blanket” between plasma and coils to absorb neutrons
Coils offset a uniform distance from W7-X plasma:
So we must scale everything up:
$$$
But at fixed plasma shape & size, coils shapes become impractical if they are too far away:
25cm separation
50cm separation
65cm separation
$$$
Najmabadi et al (2008),
Lion et al (2021)
Notes: m20160512_01_nescoutTo3DCoil.m
NESCOIL runs on nersc in 20160512-01-IllustrationOfCoilComplexityIncreasingWithSeparation

## Slide 8: In a reactor, must fit ~ 1.5m “blanket” between plasma and coils to absorb neutrons
25cm separation
50cm separation
65cm separation
Coils offset a uniform distance from W7-X plasma:
But at fixed plasma shape & size, coils shapes become impractical if they are too far away:
Hypothesis:
The coil-to-plasma distance scale for which coils are feasible is ~ the 𝛁B scale length
Notes: m20160512_01_nescoutTo3DCoils.m
NESCOIL runs on nersc in 20160512-01-IllustrationOfCoilComplexityIncreasingWithSeparation

## Slide 9: At any point, a magnetic field has multiple gradient length scales
, , , , , eigenvalues of , …
(, )
Frobenius norm
smoothly captures largest gradient ⟹ shortest length scale
I
B
Normalize so scale length gives the distance to an infinite straight wire:
Notes: E.g. pick the z direction along B, and pick the x direction along grad_perp |B|. Then Phi_{yz} = 0.

## Slide 10: To test hypothesis that 𝛁B is related to coil-plasma distance, scale length will be compared to “real” coil designs for a diverse set of 45 configurations
All scaled to same minor radius (1.7 m) and ⟨B⟩ = 5.9 T of ARIES-CS.
Coils computed with REGCOIL for a uniform-offset winding surface.
Coil-to-plasma distance & regularization computed so that Bnormal error and “coil complexity” (sheet current density) are same for all configuration.
W7-X, LHD, HSX, CFQS, CTH, CNT, NCSX, TJ-II, QPS, ATF, Precise QA/QH, CIEMAT-QI, ITER, …
Notes: m20210604_01_plotVMECWout_withFieldlineSeamAtBottom.m

## Slide 11: Main result: 𝛁B length is well correlated with real coil designs
[meters]
Coil-to-plasma distance from REGCOIL [meters]
nfp (number of field periods)
Stellarators do exist with sufficient space for a blanket,
particularly if nfp = 1 or 2.
All configs scaled to aminor = 1.7 m
Notes: coloredMoneyPlot.png, in email from John on 1012-Oct 12

## Slide 12: Main result: 𝛁B length is well correlated with real coil designs
Coil-to-plasma distance from REGCOIL [meters]
ROSE nfp5 QH
Jorge nfp1 QI
HSX with ripple
HSX without ripple
ITER
W7-X
Ku QH
Precise QAs
NCSX
Goodman nfp1 QI
CTH
W7-X with ripple
Wistell-B
Stellarators do exist with sufficient space for a blanket,
particularly if nfp = 1 or 2.
All configs scaled to aminor = 1.7 m
[meters]
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 13: The location of limiting 𝛁B length and coil complexity are also correlated spatially
Current density K [MA/m]
[m]
Limiting coil-to-coil distance occurs where scale length is smallest
Plasma surface
Coil winding surface
Notes: m20221101_01_plot_regcoil_coils_and_current_density.m
m20221031_02_plotRegcoilCurrentDensity3D.m

## Slide 14: Conclusions & future work
Internal B field, self-force, & stored energy of a coil can be computed using rapid 1D/2D integral if formulated carefully.
New method agrees with high-fidelity finite-cross-section calculations & analytic results.
Coil-to-plasma distance can be understood from scale length.
Configurations do exist with space for a blanket.
Next steps:
Apply in stellarator optimization
Test model against high-fidelity HTS calculations.
Would welcome collaboration with this!
arXiv:2310.09313, arXiv:2310.12087, arXiv:2309.11342

## Slide 15: Extra slides

## Slide 16: Main result: 𝛁B length is well correlated with real coil designs
[m]
Coil-to-plasma distance from REGCOIL [m]
Stellarators do exist with sufficient space for a blanket,
Particularly if nfp = 1 or 2.
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 17: Main result: 𝛁B length is well correlated with real coil designs
[m]
Coil-to-plasma distance from REGCOIL [m]
ROSE nfp5 QH
Jorge nfp1 QI
HSX with ripple
HSX without ripple
ITER
W7-X
Ku QH
Precise QAs
NCSX
Goodman nfp1 QI
CTH
W7-X with ripple
Wistell-B
Stellarators do exist with sufficient space for a blanket,
Particularly if nfp = 1 or 2.
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 18: Tokamak & stellarator design requires calculations for the I x B force, internal field, and stored energy
Field and force on coil 2 due to current in coil 1 can be computed quickly: 1D filament models are ok.
Tricky part is the self-field: singularity in Biot-Savart Law
azom.com
1
2
Forces ∝ B2. High B limited by support structure.
Superconductor quench limits depend on local B.
Need to be able to dissipate stored energy W = ½LI2.
Coil shapes can probably be optimized for these quantities.

## Slide 19: Simply skipping the singular point in a 1D filament calculation gives a non-converging result with significant error
Maximum |B| in the conductor [Tesla]
Circular coil
Diverges if minor radius

## Slide 20: The small coil-to-plasma separation in stellarators is a headache for engineering
“Lesson 1: A lack of generous margins, clearances and reasonable tolerance levels implies an unnecessary increase of the complexity and leads to late design changes. This has a strong impact on schedule, budget, man-power and potentially sours the relationship to funding bodies.”
Klinger et al, Fusion Engineering & Design (2013)
W7-X

## Slide 21: To test hypothesis that 𝛁B is related to coil-plasma distance, scale length will be compared to “real” coil designs for a diverse set of ~45 configurations
All scaled to same minor radius (1.7 m) and ⟨B⟩ = 5.9 T.
NCSX (li383 & c09r00)
ARIES-CS
HSX
W7-X (std, high-mirror, …)
LHD, R=3.5, 3.6, 3.75
CFQS
ML+Paul QA, QH
ML, Buller, Drevlak QA, QH
Near-axis QH
Jorge et al QI
Goodman et al QIs
ESTELL
ITER
CNT
CTH
TJ-II
QPS
ATF
CIEMAT-QI
Garabedian QA
Henneberg et al QA
Wistell-A, B
Wechsung et al QA
Giuliani et al QA
Ku & Boozer nfp=4 QH
Nuhrenberg & Zille QH
Drevlak QH
…
Notes: m20210604_01_plotVMECWout_withFieldlineSeamAtBottom.m

## Slide 22: Accurate calculation of the internal field and self-force appear to require high-dimensional integrals
Can we simplify/approximate these integrals for fast evaluation inside an optimization loop?
Force per unit length: 5D integral
Field: 3D integral
Self-inductance & stored energy: 6D integral
Notes: 20230501-01 Equations for coil force talk.lyx
20230717-01 Equations for coil force talk.lyx

## Slide 23: Analytic formulas for a circular coil show that the finite cross-section cannot be ignored
Diverges if minor radius
Could a modified 1D filament model work if we supplement it with a value for a?
Notes: 20230510-01-plot_circular_coil_mayavi
20230511-05-plot_circular_coil_mayavi_with_force_arrows

## Slide 24: Simply skipping the singular point in a 1D filament calculation gives a non-converging result with significant error
Maximum |B| in the conductor [Tesla]
Force per unit length [N / m]
Circular coil

## Slide 25: Assumption: current density J is uniform
Ok if multiple turns in both dimensions of the x-section.
Not necessarily accurate for superconductors, particularly HTS tapes.
Good enough for optimization?
Rostila et al, (2007)
J in YBCO
current
x-sectional area
unit tangent along conductor

## Slide 26: We can do the calculations for cross-sections that are either circular or rectangular
rc
u = 1
u = -1
v = -1
v = 1
b
a
p
q
rc
a
n
b
θ
ρ
Notes: 20230717-04-mayavi_plot_HSX_circular_xsection_coil_for_coordinate_definitions
20230707-01-mayavi_plot_HSX_rectangular_coil_for_coordinate_definitions
20230511-03-plot_HSX_coil_mayavi_a1cm_incomplete.png

## Slide 27: Methodology for finding an accurate reduced model
Parameterize the coil volume:
Expansion parameter: a / R ≪ 1, where R ∼ scales of curve centerline, and b ∼ a.
Introduce intermediate scale d, with a ≪ d ≪ R.
Split integrals into “near part” + “far part”.
Far part defined by . Finite cross-section can be neglected.
Near part defined by . Coil centerline can be Taylor-expanded, so integrals can be done explicitly.
Identify a 1D integral that has the same near part and far part as the above “high fidelity” calculation for a / R ≪ 1.
centerline

## Slide 28: Methodology for finding an accurate reduced model
rc
u = 1
u = -1
v = -1
v = 1
b
a
p
q
rc
a
n
b
θ
ρ
Parameterize the coil volume:
Expansion parameter: a / R ≪ 1, where R ∼ scales of curve centerline rc, and b ∼ a.
Introduce intermediate scale d, with a ≪ d ≪ R.
Split integrals into “near part” (, Taylor-expand) + “far part” (, neglect finite thickness)
Identify a 1D integral that has the same near part and far part as the above “high fidelity” calculation for a / R ≪ 1.

## Slide 29: Methodology for finding an accurate reduced model
High fidelity 3D model
New 1D filament model
a / R ≪ 1
Far contribution:
Near contribution:

## Slide 30: Limit of the 3D integral for the internal field for a / R ≪ 1
Intuition:
Leading order near-field is same as a straight wire. But corrections contribute to the force.

## Slide 31: Our new 1D filament model reproduces the same limit as the original 3D integral
Intuition:
Regularization added to Biot-Savart. Makes a difference when source and evaluation points are as close as the coil radius.
Notes: Equations from 20230501-01_Equations_for_coil_force_talk.pdf

## Slide 32: If curve centerline is a circle, the new filament model matches analytic formula for B

## Slide 33: Integrating the J x B force over the conductor cross-section, our method reduces the 5D integral for the self-force to a 1D integral
If rc is a circle
Same as analytic result

## Slide 34: A possible reduced model for the critical current?
Given a model for how the local critical current density depends on B, e.g.
Gömöry and Klinčok (2006)
estimate the global critical current as
Not self-consistent, but is it good enough to be useful?
azom.com

## Slide 35: Similarly, the inductance & stored energy can be computed accurately with only a 2D integral
6D:
2D:
for circular x-section,
for rectangular x-section.
For circular centerline, matches analytic result by
Weinstein, Annalen der Physik (1884)
Notes: 20230717-01-mayavi_plot_HSX_rectangular_coil_plain_transparent.png

## Slide 36: Calculations of internal field and self-force are also of interest for many other subjects, e.g. solar flares
NASA/SDO/Goddard

## Slide 37: Some related work
Garren & Chen, Phys. Plasmas (1994). Looked at force but not internal field. Solution is to do a 1D integral over an incomplete loop, with a specific segment removed.
Dengler, Advanced Electromagnetics (2016). Computed self-inductance using 2D integral.
Lion, Warmer, et al Nuclear Fusion (2021). Computed B in conductor by summing analytical result for rectangular prism of J.
Robin & Volpe, Nuclear Fusion (2022). Computed force for sheet current on a winding surface.
Our contribution:
Compute self-force, stored energy / inductance, and spatially-resolved internal field using only 1D/2D integrals.
Integration is over a periodic domain, so quadrature can be spectrally accurate, & can re-use points/data from other coil optimization objectives.

## Slide 38: Remaining 1D integral is still tricky since integrand has fine structure
A solution: subtract and add a function to the integrand with the same near-singular behavior that can be integrated analytically.
With singularity subtraction
Original
Notes: plot_integrand_rectangular_xsection_for_talk()
20230717-03-mayavi_plot_HSX_rectangular_coil_phi0_highlight_ab0p02.png

## Slide 39: To make integrand smooth, we subtract and add a function with the same singular behavior that can be integrated analytically.
Compute Q by Taylor expansion of integrand about .
Result:

## Slide 40: The singularity-subtraction method allows B and the force to be evaluated with very few quadrature points.
HSX coil 1
Notes: 20230717-03-mayavi_plot_HSX_rectangular_coil_phi0_highlight_ab0p02
CoilForces.plot_force_convergence_single_for_talk()
20230511-01-HSX_force_convergence_vs_nquadpoints.pdf
20230511-02-plot_HSX_coil_with_dot_mayavi_a1cm

## Slide 41: The new filament model agrees with the high-fidelity 3D integral for B in stellarator coils
HSX coil 1
|B| [T], High fidelity
|B| [T], Filament
Bz [T], High fidelity
Bz [T], Filament
The individual B components also agree:
Notes: CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi1_nn64_nb65_2023-05-11T10.06.03.780.dat")
CoilForces.plot_high_fidelity_B_vector_for_HSX_coil_for_talk("HSX_B_a0.01_rtol0.001_atol0.001_nphi2_nn30_nb31_2023-04-27T09.40.25.165.dat")
20230511-02-plot_HSX_coil_with_dot_mayavi_a1cm

## Slide 42: The 1D integral accurately approximates high-fidelity calculations for the self-force in stellarator coils
[kN / m] for HSX coil 1, @ 150 kA
High fidelity (5D integral)
1D integral
High fidelity (5D integral)
1D integral
Parameter along curve ()
Parameter along curve ()
Notes: 20230508-01-HSX_coil_force_hifi_vs_filament.pdf
Created using CoilForces.plot_hifi_force_and_1D_for_HSX_for_talk()
3D figures created using 20230508-02-plot_HSX_coil_mayavi_a1cm
And 20230508-01-plot_HSX_coil_mayavi_a10cm
The resulting png files were opened in Preview to turn the background white into transparency.

## Slide 43: Summary of main results
Internal field:
Self-force:
Notes: 20230501-01_Equations_for_coil_force_talk.pdf

## Slide 44: Methodology: Apply REGCOIL, adjust regularization λ and coil-to-plasma separation to match B error and coil current density between configurations
At fixed coil-to-plasma separation, trades off between B field error and coil complexity.
(Coil complexity)
target
At the target B field error, coil complexity increases with coil-to-plasma separation
target
Max K
[A/m]
(Coil complexity)
Coil-to-plasma distance [m]

## Slide 45: The different B scale lengths are not identical, but have similarities, e.g. all are small on the inside of concave regions
eigenvalues of
Notes: Scale_lengths.png from John’s paper

## Slide 46: Other scale lengths can be reasonably well correlated as well
Field line radius of curvature
Largest eigenvalue
Gradient of scalar B
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf