## Slide 1: Stellarator optimization Where do these shapes come from?
Matt Landreman – mattland@umd.edu, University of Maryland
Notes: https://www.youtube.com/watch?v=CJ_OBoEs3uU

## Slide 2: There is lots of freedom in the shape of a stellarator plasma and coils, which can be used to achieve many objectives
Large volume of good magnetic surfaces (not islands & chaos)
Enough rotational transform
Plasma pressure & current doesn’t modify B too much, i.e. maximum plasma pressure is not too low.
Buildable coil shapes: low curvature, large clearances
Magnetohydrodynamic (MHD) stability
Good confinement of particle trajectories
Low neoclassical transport
Low turbulent transport

## Slide 3: Outline
Optimization in general
Optimization for good flux surfaces
Quasi-axisymmetry, quasi-helical symmetry, and quasi-isodynamic
Optimization for stability & turbulence
Coil optimization: current potential and filament methods

## Slide 4: Optimization is a general technique with many applications
Given a “cost function” ,
minimize
(a.k.a. “objective function”, “loss function”)
Local minimum
Global minimum
Notes: f = @(x,y) x.*exp(-x.^2-y.^2)+(x.^2+y.^2)/20;
f = @(x,y) x.*exp(-x.^2-(y-0.5).^2)+(x.^2+y.^2)/20-0.3*exp(-4*((y+1.5).^2+x.^2));
fsurf(f,[-2,2])
set(gcf,'color','w')

## Slide 5: Optimization is a general technique with many applications
Given a “cost function” ,
minimize
(Optional) Can add constraints:
subject to ,
Suppose we want to minimize > 1 quantity, e.g. , , and .
“Scalarization”:
minimize where are weights.
(a.k.a. “objective function”, “loss function”)
Notes: f = @(x,y) x.*exp(-x.^2-y.^2)+(x.^2+y.^2)/20;
f = @(x,y) x.*exp(-x.^2-(y-0.5).^2)+(x.^2+y.^2)/20-0.3*exp(-4*((y+1.5).^2+x.^2));
fsurf(f,[-2,2])
set(gcf,'color','w')

## Slide 6: Optimization is natural to apply to stellarators
Fewer lost particles are better, but may not be able to confine every trajectory.
Lower coil curvature is better, but probably can’t make it 0.
Might not be able to achieve with good flux surfaces exactly, but we can minimize the residual .
Given a “cost function” ,
minimize
(a.k.a. “objective function”, “loss function”)
Notes: f = @(x,y) x.*exp(-x.^2-y.^2)+(x.^2+y.^2)/20;
fsurf(f,[-2,2])
set(gcf,'color','w')

## Slide 7: Some stellarator parameters are integers. These are mostly optimized by hand.
Number of “field periods”.
Number of coils.
NFP=3
NFP=4
NFP=5
Do coils link the plasma poloidally, helically, or not at all?
Do B contours link the torus toroidally (QA), helically (QH), or poloidally (QI)?
Notes: KuBoozer_2011_NF_v51_p013004 New classes of quasi-helically-symmetric stellarators.pdf
Yamaguchi_2019_NF_59_104002 QI vacuum field with helical coils.pdf

## Slide 8: There are several possible choices of parameter space to optimize in
Minimize where . What is ?
= shapes of coils:
Much of this space is very bad: not good flux surfaces, can’t evaluate physics objectives
“Free boundary equilibrium” calculations can be fragile
= shape of plasma:
Can use “fixed boundary equilibrium”, which is very reliable.
Some of parameter space corresponds to unphysical self-intersecting shapes.
Otherwise, most of this parameter space is good.
But the plasma shape is not what you build – you build coils.
Other options:
= shape of plasma and coils, = shape of magnetic axis, …

## Slide 9: Most transport-optimized stellarators have used 2 sequential optimization stages
Parameters = shape of boundary toroidal surface. Objective = physics (confinement, stability, etc.)
Parameters = coil shapes. Objective = error in B on boundary shape from stage 1.
Shape of a toroidal boundary surface (+ pressure & current vs r inside, & total B flux) determines B everywhere inside:
Notes: m20200814_01_W7XIllustrationWithCoils

## Slide 10: Most transport-optimized stellarators have used 2 sequential optimization stages
W7-X (Germany)
CFQS (China), under construction
NCSX (Princeton)
Parameters = shape of boundary toroidal surface. Objective = physics (confinement, stability, etc.)
Parameters = coil shapes. Objective = error in B on boundary shape from stage 1.
Notes: m20200814_01_W7XIllustrationWithCoils

## Slide 11: Outline
Optimization in general
Optimization for good flux surfaces
Quasi-axisymmetry, quasi-helical symmetry, and quasi-isodynamic
Optimization for stability & turbulence
Coil optimization: current potential and filament methods

## Slide 12: One goal of stellarator optimization is having field lines lie on surfaces.
Chaotic (volume-filling) B field lines would allow inside & outside to mix even without cross-B drift.
Hosoda, PRE (2009)
BAD
GOOD
Magnetic surfaces
Magnetic field lines
Notes: m20160131_DartmouthTorusFigure.m

## Slide 13: One goal of stellarator optimization is having field lines lie on surfaces.
Magnetic surfaces (a.k.a flux surfaces) can be visualized with a “Poincare plot”:
J P Kremer,
PhD thesis, Columbia
Good
Islands, where ι is rational
Chaos
Not so good

## Slide 14: How much rotational transform do you want?
Islands
Avoid rationals like ι = 1 or ½: islands form there.
So, maybe want low “magnetic shear” = |∇ι|.
Or, maybe want high magnetic shear since it makes islands thin. (width ∝ |∇ι|-1/2)
Larger ι means:
Thinner orbits, so better confinement.
B changes less due to plasma current. (Higher “equilibrium β limit”.)
But, more complicated coils.
Notes: 20200812-01-plotIotaProfiles.pdf

## Slide 15: Perhaps the first type of stellarator optimization was to achieve good flux surfaces
Reproduction of Cary & Hanson (1986) by Rogerio Jorge
Unoptimized
Optimized
R [m]
R [m]
Z [m]
Z [m]
Parameter space x = Fourier modes of coil shapes. Cost function f = square of “Greene’s residue”

## Slide 16: Optimization for good flux surfaces continues to be a principle behind recent stellarators
CTH:
(Compact Toroidal Hybrid, at Auburn)
CNT (Columbia Non-neutral Torus):
Optimize expected volume over possible coil position errors
Pedersen (2004), Hammond (2016)

## Slide 17: Outline
Optimization in general
Optimization for good flux surfaces
Quasi-axisymmetry, quasi-helical symmetry, and quasi-isodynamic
Optimization for stability & turbulence
Coil optimization: current potential and filament methods

## Slide 18: Reminder: the ∇B and curvature drifts make confinement challenging
Ions drift up: they are not confined!
Magnetic field line
Particle trajectory
Guiding center trajectory
Notes: m20230807_01_illustrationOfGuidingCenterDrift.m – flip horizontally

## Slide 19: Mirror force: particles are pushed away from regions of high |B|
Ion trajectory
v×B force has slight  component
B field lines
A few particles with very small v|| = v⋅B “bounce” and are “trapped” in low-|B| regions.
|B|
Notes: m20200812_02_orbitsInATokamak.m

## Slide 20: Flux surfaces are not enough: Trapped particles are not confined without a further condition like “quasisymmetry” or “omnigenity”
In general: trapped particles do not sample the whole surface, so cross-field drift does not average to 0.
One solution is quasisymmetry: make B(r, 𝜃, 𝜑) = B(r, M𝜃−N𝜑) for special angles 𝜃, 𝜑.
B
Symmetry direction
⟹ Conserved quantity.
⟹ Drift averages to 0.
⟹ Large neoclassical transport.
Su et al (2020)

## Slide 21: Lemma: deeply trapped particles move so |B| is constant
Distance along a field line
Deeply trapped particles
so the drift

## Slide 22: For low neoclassical transport, recent stellarators have come in 3 flavors
Trapped particles should drift toroidally, helically, or poloidally on a surface.
B contours on a surface have the same topology as these drifts.
E.g., particles with v||=0
move along a constant-B contour:
Toroidal:
Helical:
Poloidal:
Notes: https://commons.wikimedia.org/wiki/File:Torus_illustration.png

## Slide 23: For low neoclassical transport, recent stellarators have come in 3 flavors
Trapped particles should drift toroidally, helically, or poloidally on a surface.
B contours on a surface have the same topology as these drifts.
Toroidal: “QA” = Quasi-axisymmetric
Helical: “QH”= Quasi-helically symmetric
Poloidal: “QI”= Quasi-isodynamic
Field lines
|B| contours (slightly idealized)
Trapped particle
Notes: m20200812_02_3TypesOfOptimizedStellarator_gif.m

## Slide 24: Pros and cons of the 3 classes
QA:
+ Lowest aspect ratio
+ Fewest coils, largest clearances
+ Large bootstrap current increases iota
- Wider orbits mean worse confinement
- Large current may contribute to MHD instability
QH:
+ Extremely good confinement
+ Can build on experience with HSX
- Seems to require high aspect ratio and many coils
? Intermediate bootstrap current between QA and QI
QI:
+ Low bootstrap current means high robustness to different pressure profiles
+ Can use island divertor
+ Can build on experience from W7-X
- Seems to require high aspect ratio and many coils
- Optimization is generally trickier

## Slide 25: There has been great progress recently in optimizing stellarator neoclassical confinement
Since 2021
Trajectories of fusion-produced distribution of alpha particles followed in many magnetic configurations, all scaled to reactor size and |B|:
Fraction of alpha-particle energy lost before thermalization
Landreman et al, Phys Plasmas (2022).

## Slide 26: The parameter space for stage-1 optimization is typically a set of Fourier amplitudes for the boundary surface in cylindrical coordinates
𝜃
Magnetic field lines
Parameterization of boundary surface:
Parameter space for optimization:
= standard cylindrical angle, = number of field periods

## Slide 27: Quasisymmetry is a sufficient (though not necessary) condition for confinement, & a useful surrogate
“Boozer angles”
B = B(s, 𝜃 − N 𝜑)
𝜃
𝜑
Constant s = normalized toroidal flux
Magnetic field lines
Boundary aspect ratio
For quasi-axisymmetry,
N = 0.
For quasi-helical symmetry,
N is the number of field periods,
e.g.
N = 4
here
Objective:

## Slide 28: Example of quasi-axisymmetry optimization
ML & Paul, Phys Rev Lett (2022)

## Slide 29: Example of quasi-helical symmetry optimization
ML & Paul, Phys Rev Lett (2022)

## Slide 30: There has been similar recent progress in finding quasi-isodynamic configurations
Sanchez et al (2023)
Dudt et al (2023)
Goodman et al (2023)
Jorge et al (2022)
Mata et al (2022)

## Slide 31: Outline
Optimization in general
Which parameter space to optimize in?
Quasi-axisymmetry, quasi-helical symmetry, and quasi-isodynamic
Optimization for stability & turbulence
Coil optimization: current potential and filament methods

## Slide 32: Stellarator geometry can be optimized for MHD stability
Sanchez et al, Plasma Phys. Control. Fusion (2000)
Types of MHD stability calculations, in increasing complexity:
Magnetic well & Mercier’s criterion (interchange)
Ballooning modes (short wavelength ⟂ to B)
Finite wavelength (everything)
Growth rate of ballooning modes
(minor radius)
Cote et al, (2019)

## Slide 33: Optimization for reduced turbulence has mostly used simplified proxies in the cost function
Nunami 2017
Turbulent heat flux can be simulated, but it is computationally expensive and noisy
not good for an objective function
Time (normalized)
Turbulent heat flux (code units)

## Slide 34: Optimization for reduced turbulence has mostly used simplified proxies in the cost function
Mynick et al, Physical Review Letters (2010)
NCSX (unoptimized)
NCSX (unoptimized)
optimized
optimized
optimized
Time (normalized)
Turbulent heat flux (code units)

## Slide 35: The first optimizations with nonlinear turbulence calculations in the objective are becoming possible
By Patrick Kim (Maryland undergraduate!)
time

## Slide 36: Outline
Optimization in general
Optimization for good flux surfaces
Quasi-axisymmetry, quasi-helical symmetry, and quasi-isodynamic
Optimization for stability & turbulence
Coil optimization: current potential and filament methods

## Slide 37: Calculating the currents that produce a given B is an “ill-posed inverse problem”: solution is not unique.
Some kind of ‘regularization’ is needed to exclude solutions like this:
Actually a good thing:
There is a lot of freedom in coil design
Notes: Figure created using m20160506_01_W7X_illustrationForBDISTRIBTalk.m

## Slide 38: Finding coils that produce a given B is analogous to fitting data with a polynomial
As polynomial degree increases, fit is closer to data but less ‘regular’.
Polynomial degree is the ‘regularization parameter’.

## Slide 39: Current potential methods: NESCOIL & REGCOIL
Pros:
Linear least-squares: no local optima besides the global one.
Only 2 parameters to vary: coil-to-plasma distance and .
ML, Nuclear Fusion (2017).
Regcoil: Consider sheet current on a “coil winding surface”
Surface current
Normal to winding surface
“current potential”
B field error
Regularization parameter
Coil complexity
contours = coils
Plasma
surface
Coil
surface
distance between coils
Cons:
Neglects ripple from discrete coils.
Coils can’t move in 3rd dimension.
Notes: m20221031_01_plot_regcoil_coils_and_surfaces.png

## Slide 40: In stage-2 coil optimization, there is a trade-off between field accuracy and coil simplicity
High regularization λ:
Simpler coils
but large field error
Low regularization λ:
Complicated coils
but small field error

## Slide 41: Filament coil optimization
Assume plasma shape has already been optimized, so target B field is known.
Coils represented as space curves.
Design variables: Fourier modes of Cartesian components.
Objective:
Does account for B ripple from discreteness of coils.
Non-convex, so there are multiple local minima. Need good initial guess.
+…
Match target B
Regularization
Zhu, Hudson, et al, Nuclear Fusion (2018).

## Slide 42: Open questions for stellarator optimization
How best to combine coil and plasma design?
How to find designs that tolerate errors in coil shape/position?
How to avoid getting stuck in little local minima? How to find global optima?
How to optimize for expensive & noisy objectives (turbulence & fast-particle confinement)?
How to balance multiple competing objectives?
How to optimize coil topology?
How to find configurations that are flexible?
  Good confinement for different plasma pressures.
  Ability to tune physics properties by changing coil currents.

## Slide 43: More resources
Introductory papers:
Imbert-Gerard, Paul, & Wright, https://arxiv.org/abs/1908.05360
Helander, http://dx.doi.org/10.1088/0034-4885/77/8/087001
Summer schools:
https://hiddensymmetries.princeton.edu/summer-school/summer-school-2020/schedule
https://hiddensymmetries.princeton.edu/summer-school/summer-school-2019/schedule
https://gss.pppl.gov/2021/
https://suli.pppl.gov/2022/course/index.html
https://suli.pppl.gov/2021/course/index.html
https://suli.pppl.gov/2020/course/index.html
https://suli.pppl.gov/2019/course/index.html
Open-source software:
https://github.com/PrincetonUniversity/STELLOPT
https://desc-docs.readthedocs.io/
https://simsopt.readthedocs.io/
https://github.com/landreman/regcoil
https://gitlab.com/wistell/StellaratorOptimization.jl