## Slide 1: Inverse magnetostatics & its application to stellarator optimization
Matt Landreman1, Alan Kaptanoglu2, John Kappel1, Gabriel Langlois2, Dhairya Malhotra3
1. University of Maryland 2. NYU Courant 3. Flatiron Institute
Notes: https://www.youtube.com/watch?v=CJ_OBoEs3uU

## Slide 2
Inverse magnetostatics:
We want a certain magnetic field B in a region Ω.
Find an arrangement of electric currents outside Ω that produce B.
I.e., invert the Biot-Savart Law
Notes: https://media.cnn.com/api/v1/images/stellar/prod/220705075914-01-large-hadron-collider-file.jpg?c=original
https://www.lhc-closer.es/webapp/files/1435504063_7a5913ddba2ffceaacc3026f44c4b624.jpg

## Slide 3
Example: Particle accelerators
Inverse magnetostatics:
We want a certain magnetic field B in a region Ω.
Find an arrangement of electric currents outside Ω that produce B.
Notes: https://media.cnn.com/api/v1/images/stellar/prod/220705075914-01-large-hadron-collider-file.jpg?c=original
https://www.lhc-closer.es/webapp/files/1435504063_7a5913ddba2ffceaacc3026f44c4b624.jpg

## Slide 4
Inverse magnetostatics:
We want a certain magnetic field B in a region Ω.
Find an arrangement of electric currents outside Ω that produce B.
Example: Magnetic resonance imaging
Poole & Bowtell (2007)
Notes: https://www.directradiology.com.au/media/jl3df5fy/capitol-radiology-76.jpg

## Slide 5
Inverse magnetostatics:
We want a certain magnetic field B in a region Ω.
Find an arrangement of electric currents outside Ω that produce B.
Example: Magnetic confinement fusion
Electromagnetic coils
Plasma
Magnetic field lines
Stellarator
Tokamak→
Notes: https://www.epj-conferences.org/articles/epjconf/pdf/2020/22/epjconf_lnes2020_00013.pdf
https://www.researchgate.net/profile/Gary-Taylor-4/publication/280601072/figure/fig4/AS:284555547299848@1444854737441/Free-boundary-vacuum-calculations-of-some-of-the-achievable-plasma-configurations-in-MAST.png

## Slide 6: Outline
Background & previous approaches
Current voxels: topology optimization for electromagnets
A A Kaptanoglu, G P Langlois, & ML, Comp Meth Appl Mech Engr (2023)
Bounding the distance to the coils
J Kappel, ML, & D Malhotra, arXiv:2309.11342 (2023)

## Slide 7: Outline
Background & previous approaches
Current voxels: topology optimization for electromagnets
A A Kaptanoglu, G P Langlois, & ML, Comp Meth Appl Mech Engr (2023)
Bounding the distance to the coils
J Kappel, ML, & D Malhotra, arXiv:2309.11342 (2023)

## Slide 8: Most transport-optimized stellarators have used 2 sequential optimization stages
Parameters = shape of boundary toroidal surface. Objective = physics (confinement, stability, etc.)
Parameters = coil shapes. Objective = error in B on boundary shape from stage 1.
Shape of a toroidal boundary surface (+ pressure & current vs r inside, & total B flux) determines B everywhere inside:
Notes: m20200814_01_W7XIllustrationWithCoils

## Slide 9: Most transport-optimized stellarators have used 2 sequential optimization stages
W7-X (Germany)
CFQS (China), under construction
Parameters = shape of boundary toroidal surface. Objective = physics (confinement, stability, etc.)
Parameters = coil shapes. Objective = error in B on boundary shape from stage 1.
Notes: m20200814_01_W7XIllustrationWithCoils

## Slide 10: Calculating the currents that produce a given B is an ill-posed inverse problem: solution is not unique.
Some kind of regularization is needed to exclude solutions like this:
Actually a good thing:
There is a lot of freedom in coil design
Notes: Figure created using m20160506_01_W7X_illustrationForBDISTRIBTalk.m

## Slide 11: Current potential methods: REGCOIL
Pros:
Linear least-squares: no local optima besides the global one.
Only 2 parameters to vary: coil-to-plasma distance and .
ML, Nuclear Fusion (2017).
Regcoil: Consider sheet current on a “coil winding surface”
Surface current
Normal to winding surface
“current potential”
B field error
Regularization parameter
Coil complexity
contours = coils
Plasma
surface
Coil
surface
distance between coils
Cons:
Neglects ripple from discrete coils.
Limited flexibility in 3rd dimension.
Notes: m20221031_01_plot_regcoil_coils_and_surfaces.png

## Slide 12: In stage-2 coil optimization, there is a trade-off between field accuracy and coil simplicity
High regularization λ:
Simpler coils
but large field error
Low regularization λ:
Complicated coils
but small field error

## Slide 13: Filament coil optimization
Coils represented as space curves.
Design variables: Fourier modes of Cartesian components.
Objective:
Does account for B ripple from discreteness of coils.
Non-convex, so there are multiple local minima. May need good initial guess.
+…
Match target B
Regularization
Zhu, Hudson, et al, Nuclear Fusion (2018).

## Slide 14: Outline
Background & previous approaches
Current voxels: topology optimization for electromagnets
A A Kaptanoglu, G P Langlois, & ML, Comp Meth Appl Mech Engr (2023)
Bounding the distance to the coils
J Kappel, ML, & D Malhotra, arXiv:2309.11342 (2023)

## Slide 15: Current voxels: topology optimization for inverse magnetostatics
Coil topology is an output rather than input.
Generalize REGCOIL to lift restriction that currents lie on specified surface.
Preserve REGCOIL advantages of linearity/convexity as far as possible.
Yamaguchi (2019)
Kaptanoglu, Langlois, & ML, arXiv:2306.12555 (2023)

## Slide 16: New topology optimization method for electromagnetic coils
Pre-define grid of voxels where current might flow.
Current density J in each voxel represented by basis of 5 divergence-free functions. Amplitudes are the design variables.
Charge conservation at each cell face gives linear equality constraints.
Alternative:
Design variables are the fluxes through faces. Linear constraints enforce 0 net flux in each volume.

## Slide 17: New topology optimization method for electromagnetic coils
Given basis functions, B can be computed by Biot-Savart Law:
Without sparsity-promoting terms, problem is linear.
With ℓ1 sparsity, problem remains convex.
With ℓ0 sparsity, good algorithms exist.
Match target B
Regularization
Minimize objective:

## Slide 18: The ℓ0-regularized problem is solved using the “relax & split” method
Original problem:
s.t. .
Relaxed problem:
s.t. .
Iterate:
s.t. .
Linear least-squares with linear constraints.
Solved with MINRES + approximate Schur complement preconditioner.
Equivalent to a proximal operator.
Solved exactly by but with small entries set to 0.
Zheng, Askham, Brunton, Kutz, Aravkin, IEEE Access (2019), Champion, Zheng, Aravkin, Brunton, Kutz, IEEE Access (2020)

## Slide 19: In axisymmetry, without sparsity terms, expected currents are recovered
Notes: Image in an email from Alan on Sept 23, 2023, titled “current voxels picture”

## Slide 20: With sparsity objective included, currents coalesce into discrete coils

## Slide 21
Larger l0 coefficient

## Slide 22
Larger l0 coefficient
The new current voxel for inverse magnetostatics enables topologically unconstrained 3D solutions with quadratic, convex, or structured objectives.

## Slide 23: Outline
Background & previous approaches
Current voxels: topology optimization for electromagnets
A A Kaptanoglu, G P Langlois, & ML, Comp Meth Appl Mech Engr (2023)
Bounding the distance to the coils
J Kappel, ML, & D Malhotra, arXiv:2309.11342 (2023)

## Slide 24: How far away can the magnets be?
Notes: Figure created using m20160506_01_W7X_illustrationForBDISTRIBTalk.m

## Slide 25: The small coil-to-plasma separation in stellarators is a headache for engineering
“Lesson 1: A lack of generous margins, clearances and reasonable tolerance levels implies an unnecessary increase of the complexity and leads to late design changes. This has a strong impact on schedule, budget, man-power and potentially sours the relationship to funding bodies.”
Klinger et al, Fusion Engineering & Design (2013)
W7-X

## Slide 26: In a reactor, must fit ~ 1.5m “blanket” between plasma and coils to absorb neutrons
Coils offset a uniform distance from W7-X plasma:
So we must scale everything up:
$$$
But at fixed plasma shape & size, coils shapes become impractical if they are too far away:
25cm separation
50cm separation
65cm separation
$$$
Najmabadi et al (2008),
Lion et al (2021)
Notes: m20160512_01_nescoutTo3DCoil.m
NESCOIL runs on nersc in 20160512-01-IllustrationOfCoilComplexityIncreasingWithSeparation

## Slide 27: In a reactor, must fit ~ 1.5m “blanket” between plasma and coils to absorb neutrons
25cm separation
50cm separation
65cm separation
Coils offset a uniform distance from W7-X plasma:
But at fixed plasma shape & size, coils shapes become impractical if they are too far away:
Hypothesis:
The coil-to-plasma distance scale for which coils are feasible is ~ the 𝛁B scale length
Notes: m20160512_01_nescoutTo3DCoils.m
NESCOIL runs on nersc in 20160512-01-IllustrationOfCoilComplexityIncreasingWithSeparation

## Slide 28: At any point, a magnetic field has multiple gradient length scales
, , , , , eigenvalues of , …
(, )
Frobenius norm
smoothly captures largest gradient ⟹ shortest length scale
I
B
Normalize so scale length gives the distance to an infinite straight wire:
Notes: E.g. pick the z direction along B, and pick the x direction along grad_perp |B|. Then Phi_{yz} = 0.

## Slide 29: The different B scale lengths are not identical, but have similarities, e.g. all are small on the inside of concave regions
eigenvalues of
Notes: Scale_lengths.png from John’s paper

## Slide 30: To test hypothesis that 𝛁B is related to coil-plasma distance, scale length will be compared to “real” coil designs for a diverse set of ~45 configurations
All scaled to same minor radius (1.7 m) and ⟨B⟩ = 5.9 T.
NCSX (li383 & c09r00)
ARIES-CS
HSX
W7-X (std, high-mirror, …)
LHD, R=3.5, 3.6, 3.75
CFQS
ML+Paul QA, QH
ML, Buller, Drevlak QA, QH
Near-axis QH
Jorge et al QI
Goodman et al QIs
ESTELL
ITER
CNT
CTH
TJ-II
QPS
ATF
CIEMAT-QI
Garabedian QA
Henneberg et al QA
Wistell-A, B
Wechsung et al QA
Giuliani et al QA
Ku & Boozer nfp=4 QH
Nuhrenberg & Zille QH
Drevlak QH
…
Notes: m20210604_01_plotVMECWout_withFieldlineSeamAtBottom.m

## Slide 31: Methodology: Apply REGCOIL, adjust regularization λ and coil-to-plasma separation to match B error and coil current density between configurations
At fixed coil-to-plasma separation, trades off between B field error and coil complexity.
(Coil complexity)
target
At the target B field error, coil complexity increases with coil-to-plasma separation
target
Max K
[A/m]
(Coil complexity)
Coil-to-plasma distance [m]

## Slide 32: Main result: 𝛁B length is well correlated with real coil designs
[m]
Coil-to-plasma distance from REGCOIL [m]
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 33: Main result: 𝛁B length is well correlated with real coil designs
[m]
Coil-to-plasma distance from REGCOIL [m]
ROSE nfp5 QH
Jorge nfp1 QI
HSX with ripple
HSX without ripple
ITER
W7-X
Ku QH
Precise QAs
NCSX
Goodman nfp1 QI
CTH
W7-X with ripple
Wistell-B
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 34: Other scale lengths can be reasonably well correlated as well
Field line radius of curvature
Largest eigenvalue
Gradient of scalar B
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 35: The location of limiting 𝛁B length and coil complexity are also correlated spatially
Current density K [MA/m]
[m]
Limiting coil-to-coil distance occurs where scale length is smallest
Plasma surface
Coil winding surface
Notes: m20221101_01_plot_regcoil_coils_and_current_density.m
m20221031_02_plotRegcoilCurrentDensity3D.m

## Slide 36
Conclusions:
The new current voxel for inverse magnetostatics enables topologically unconstrained 3D solutions with quadratic, convex, or structured objectives.
The maximum coil separation can be understood from the scale length .
Questions:
Is there a more efficient solver for the current voxel system?
Can the current voxel method be generalized for more flexible geometry (tetrahedra?)
Is a useful objective function to enable larger coil separation?
Besides , are there other metrics to predict coil separation?
Improvements in algorithms for inverse magnetostatics can translate to significant benefits for fusion, accelerators, MRI, etc.

## Slide 37: Extra slides

## Slide 38: 2D example
3 basis functions per cell, 12 degrees of freedom, 11 unique constraints

## Slide 39: At any point, a magnetic field has multiple gradient length scales
, , , , , eigenvalues of , …
(, )
We can get some insights by considering vacuum fields:
so is a symmetric 3×3 matrix ⟹ 6 degrees of freedom.
-1 degree of freedom since .
Frobenius norm
captures largest gradient ⟹ shortest length scale
Some entries can be made to vanish by rotating the coordinate system.
Notes: E.g. pick the z direction along B, and pick the x direction along grad_perp |B|. Then Phi_{yz} = 0.

## Slide 40: The 𝛁B scale lengths can be normalized so that in the case of an infinite straight wire, they give the distance to the wire
I
B
Notes: 20221030-01-mayavi_wire_for_grad_B_talk

## Slide 41: The different B scale lengths are not identical, but have similarities, e.g. all are small on the inside of concave regions
eigenvalues of
Notes: “scale.png” in an email from John Kappel on 2022-11-05

## Slide 42: Main result: 𝛁B length is well correlated with real coil designs
[m]
All configurations scaled to same minor radius
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 43: Main result: 𝛁B length is well correlated with real coil designs
[m]
Wistell-B
Jorge nfp1 QI
Goodman nfp1 QI
HSX with ripple
HSX without ripple
ESTELL
ITER
Wistell-A
W7-X
ROSE nfp5 QH
Precise QA
NCSX
All configurations scaled to same minor radius
Notes: 20221103-01-plot_Kappel_results_grad_B_tensor.pdf

## Slide 44: Regcoil coil-to-plasma distance is actually well correlated with other definitions of B length scale too
All configurations scaled to same minor radius
[m]
Notes: 20221105-01-plot_Kappel_results_grad_mod_B.pdf

## Slide 45: Regcoil coil-to-plasma distance is actually well correlated with other definitions of B length scale too
[m]
All configurations scaled to same minor radius
Notes: 20221105-01-plot_Kappel_results_grad_mod_B.pdf