## Slide 1: Theory of Filtration, Dialysis, and Membranes
Team 4
Daniel Ivanov, Aaron Forest, Jillian Schwartz, Catherina Samson

## Slide 2: Fundamentals of Filtration
Separate solid particles (impurities) from a fluid
Employs a filter medium that is porous
  Molecules larger than pores are trapped
  Molecules smaller than pores pass through filter
Industry Examples:
  Oil filtration
  Catalyst recovery
  Water treatment
https://en.wikipedia.org/wiki/Filtration

## Slide 3: Fundamentals of Membrane Separations
Utilizes semi-permeable membranes to selectively separate certain components from a fluid mixture
Separation is based on differences in molecule size, concentration, or charge
Industry Examples:
  Nitrogen production from air
  Pharmaceutical purification
  Dairy processing
https://openmembranedatabase.org/membrane-science/

## Slide 4: Fundamentals of Dialysis
Procedure used to remove waste products, excess fluids, and electrolytes
Separation based on concentration gradient
Commonly used in medical settings for kidney related issues
https://www.medbroadcast.com/procedure/getprocedure/hemodialysis

## Slide 5: Driving Forces
Concentration Gradient
  Solute concentrations on either side of a separator can drive the diffusion of solutes through the separator
Pressure Difference
  Pressure difference across a separator can drive the movement of solvents or solutes through the separator
Electric Potential
  Voltage difference across a separator can drive the movement of charged particles through ion-selective separator

## Slide 6: Design Equations: Porous Diffusion
Membrane thickness
Concentration gradient across the membrane
Flux of solute i across the membrane for liquid diffusion through pores
Effective Diffusion
Unitless restrictive factor
Porosity
Diffusion coefficient
Tortuosity
Molecular diameter/pore diameter
All equations taken from Seader, et al.

## Slide 7: Design Equations: Bulk Diffusion
Flux of solute i across the membrane for bulk flow where 𝜏 = 1
Flux of solute i across the membrane for bulk flow where 𝜏 > 1
Density of solvent
Path of pore
Pressure gradient across the membrane
Specified surface area
Viscosity of solvent
Pore diameter
All equations taken from Seader, et al.

## Slide 8: Design Equations: Dialysis
Overall mass-transfer coefficient
Permeability
Differential rate of solute mass transfer across the membrane
Total membrane surface area
All equations taken from Seader, et al.

## Slide 9: Overview of Haber-Bosch Process
https://byjus.com/chemistry/haber-process

## Slide 10: How are Filtration, Dialysis, and Membranes used in Ammonia Production?
Filtration, dialysis, and membranes function in very similar manners
Dialysis can be used to obtain specific ammonia concentrations/compositions
Filtration can be used to prep/purify feed streams
Membranes can be used to capture carbon dioxide produced during the hydrogen production

## Slide 11: Filtration
Short history of ammonia process – past, present and future. AmmoniaKnowHow. (n.d.). https://ammoniaknowhow.com/short-history-of-ammonia-process-past-present-and-future/

## Slide 12: Membrane
https://netl.doe.gov/
Notes: Goal: ammonia from coal with membrane-based CO2 removal
Used in the process of gasification to get H2 for ammonia production
Capture CO2 for sequestration
Coal + O2 → syngas H2
HRSG: heat recovery steam generator
ASU: air separation unit

## Slide 13: Dialysis
Short history of ammonia process – past, present and future. AmmoniaKnowHow. (n.d.). https://ammoniaknowhow.com/short-history-of-ammonia-process-past-present-and-future/

## Slide 14: Questions??

## Slide 15: Citations
Introduction to ammonia production. AIChE. (2019, February 1). https://www.aiche.org/resources/publications/cep/2016/september/introduction-ammonia-production
Preparing your download. ScienceDirect.com. (n.d.). https://www.sciencedirect.com/science/article/pii/S1876610217319525/pdf?md5=fac2cbbdef2b9374983d8f6cca5d1803&pid=1-s2.0-S1876610217319525-main.pdf
Short history of ammonia process – past, present and future. AmmoniaKnowHow. (n.d.). https://ammoniaknowhow.com/short-history-of-ammonia-process-past-present-and-future/
Seader, J. D., et al. Separation Process Principles. John Wiley & Sons, Inc., 2011.